## Slide 1: 24/47 GHz TWT Power Supplies
W5LUA
February 6, 2021

## Slide 2: VPW2931 Power Supplies
This one powers an Alelco 100 watt 24 GHz tube for terrestrial
This power supply had been used for years to power my 30 watt 47 GHz tube but last November the PS developed a HV short that took out some logic circuitry
Auxiliary power supply for lowering collector voltages for my tube

## Slide 3: VPW2838 Power Supply
This power supply has potential but all I have done is an initial turn-on.
Until recently, we did not have a lot of information on this power supply

## Slide 4: VPW2874 Power Supply
I built an external auxiliary collector power supply that allows me to optimize voltages for my 47 GHz tube.
This power supply has the most potential and is the one I am modifying at present for my 47 GHz twt. This unit can supply 24 KV at 200 ma for 28 GHz applications
All 3 types of these supplies were designed for single depressed collector 100W 28 GHz tubes.
My 47 GHz tube is a dual depressed collector tube with different voltages

## Slide 5: Power Supply & TWT
Presently working rise time issues when switching off tube. Small spike in helix current due to defocusing of helix during transition.
The 90 ft of cable has a measured 4400 pF of capacitance from grid to cathode. The grid supply is a relatively high impedance source.

## Slide 6: Auxiliary PS for VPW2874 PS
Resistors to drop filament voltage at tube to 5.6V
Rowe HV connector from 90 ft cable to twt out at feedpoint
18 X 200V 50 watt Zener diodes drop collector voltage from a nominal 7200V down to 5600V for collector #1 and 3600V for collector #2. Resistors are used to drop collector #2 voltage to 3500V. Collector #2 current ~ 44mA. All voltages are referenced to cathode which is sitting at -14200V w.r.t. ground

## Slide 7: Power Supply Dummy Load
Helix Load
Collector Load
Filament Load
High Voltage switch with tag line
100X HV Probe
15kv Wire
15kv Rowe HV connector
1”X 12” Wood

## Slide 8: 47 GHz EME
2.4 m Offset fed dish fed with W2IMU Feed
Dish also used on 24 & 76 GHz
47 GHz xvtr with 30 watt TWT
24 GHz XVTR
24 GHz 100W TWT

## Slide 9: Closeup of 47 GHz XVTR
JA8CMY LNA
NF < 2 dB
DB6NT XVTR
DB6NT LO

## Slide 10: 47 GHz TWT Breakout Box

## Slide 11: 47 GHz W2IMU Feed with Flare

## Slide 12: Next Steps
Building conditioning circuits for the cathode and grid lines out at the twt.
If anyone has any experience with any of these power supplies, I would like to hear from you w5lua@sbcglobal.net
Run further EME tests with JA1WQF.
See you off the moon.
73 Al