## Slide 1: Flyswatter Antenna on 5760 MHz
W5LUA
February 6, 2021

## Slide 2: Introduction
I wanted to put up a dedicated antenna for 5760 MHz…..
My flyswatter has worked well on 47 and 76 GHz so why not 5760 MHz?
Next step was to check out the W1GHz Periscope Antenna Gain Calculator.
Then do I have enough coax/waveguide to get out to the base of the rotating tower?

## Slide 3: Periscope or Flyswatter Antenna

## Slide 4: Lower Equipment Platform
Two 6 ft Pieces 2 inch angle , ¼ inch thickness
Two guy wires and turnbuckles used for support and alignment

## Slide 5: Platform with 77 & 47 GHz Xvtrs
2 Transverters taking advantage of the larger than optimum reflector
I installed “Wings” on transverters so they can slide on the equipment platform
Sears Digital Torpedo Level and shims used to insure transverters are in good alignment with reflector
77 GHz
47 GHz
GPS Ant

## Slide 6: Stop Sign Flyswatter Reflector
Built and originally used by KA5BOU
Small actuator used to optimize tilt from nominal 45 degree. Craig rotated the reflector since he used the reflector on a non-rotating tower. This also meant that he had to rotate the polarity of his source antenna to maintain horizontal polarity with respect to the horizon

## Slide 7: W1GHZ Periscope Antenna Gain Calculator
Dish diameter = 30 inches
Reflector spacing ~ 45 ft
Reflector above ground ~ 51 ft
Flyswatter Aperture ~ 32 inches
Most Important

## Slide 8: 30 inch Dish for 5760 MHz
Feed is WB5LUA Dual Band 5/10 GHz Feed

## Slide 9: Rotating Tower for 6m through 23 cm + Flyswatter

## Slide 10: Radome
Radome purchased at Tractor Supply in Celina..
TSC 25 gal heavy duty round stock tank
SKU 222987099
$34.99
Loss at 5760 MHz measured at 2 to 3 dB
Has already proven to protect dish from hail on Jan 24th 2021

## Slide 11: Pressurized WR-137 Rigid and Flex
31ft Rigid w/g 1 dB loss + 12ft Flex w/g .6 dB loss + 2 X 1/2” SF jumpers .9 dB loss for a total loss of 2.5 dB – Run with ½ in LDF and Superflex would be 3.5 dB loss….still not bad for 5760 MHz

## Slide 12: Waveguide Pressurization
Aquarium pumps
Desiccant Jar
Air manifold with pressure gauges
I would like to find something better than aquarium pumps!

## Slide 13: W5HN 5760 MHz Beacon key down

## Slide 14: W5AFY 5760 MHz QSL
170 mile DX

## Slide 15
For further consideration to help others get a 10 GHz antenna up 20 ft…..

## Slide 16: 10 GHz Flyswatter at 20 ft.
Dish diameter = 18 inches
Reflector spacing ~ 20 ft
Flyswatter Aperture ~ 24 inches

## Slide 17
Any Questions?