## Slide 1: Desert, TX Beacon Update
W5LUA & AA5AM
March 6, 2021

## Slide 2: Scott plugging holes in shack
Location EM13sj
Lat 33.382185 N
Long 96.4206 W
8ft X 12ft air conditioned fiberglass building

## Slide 3: Lighting & W5HN Beacons

## Slide 4: 6 & 2 m W5HN Beacons
Hamtronics FM strips with on/off keying
2m 144.280.2 MHz 1.5 watts
6m 50.072.4 MHz 1 watt
WW2R/G4FRE beacon IDer

## Slide 5: 450 ft Tower
Our 6/2 m M2 halos are at 180 ft
My son Bryan N5QGH and I installed these about 20 plus years ago – I have no intention of climbing to this height ever again.
I plan to install a “temporary” new 6 m dipole antenna at about the 60 ft level and feed with about 70 ft of Belden 8214 with a measured 1 dB loss. Exact directional orientation TBD. We have been given the approval to put up the new antenna

## Slide 6: 6m dipole built by Bob Gormley WA5YWC

## Slide 7: Future Plans
Plan is to install WY6K’s CW/FT8 2m beacon soon. The existing 2m beacon will be back up.
Install 6m dipole next week.
Consider adding Internet capability to allow for changing power levels, antennas, etc.
and……

## Slide 8: How about some additional microwave beacons?
Second 10 GHz beacon, could be DB6NT or a ZL PLL board with built in keyer and add a several hundred milliwatt PA. Install at 60 ft level. Would need an omni beacon antenna such as a slot antenna. GPS locked?
47 GHz beacon
76 GHz beacon
Other bands of interest to club members?

## Slide 9: www.heywhatsthat.com
The following slides show panoramic views at the Desert tower at various elevations
Views provided by www.heywhatsthat.com

## Slide 10: Desert tower view 6ft above ground
Tower is in a bit of a hole despite the higher areas on same property

## Slide 11: Desert Tower View @ 450ft

## Slide 12: Desert Tower View @ 180 ft
2 & 6 m antennas are at this height

## Slide 13: Desert Tower View @ 60 ft
Proposed height for second 6 m antenna

## Slide 14: Desert Tower View @ 15ft
Location of ISP tower that we propose using for internet – approximately 10 miles south of Desert tower
Lat 33.246254 N
Long 96.425726 W
Desert Tower
Lat 33.382185 N
Long 96.4206 W

## Slide 15: Summary
Nice to have the 2m beacon operational again.
Signal has been reported from as far away as Dan W5AFY EM04id DX = 171 miles