## Slide 1: A $20 WiFi Spectrum Analyzer
The Proxim 7400 RangeLAN2

## Slide 2: Why would I want a WiFi spectrum analyzer ?
To visually display 802.11 network signals
To display signals interfering with an 802.11 network
A general purpose tool for observing the 2.4 GHz ISM band

## Slide 3: 802.11 Spectrum Review

## Slide 4: 802.11b/g Frequency Mapping
802.11b/g Channel-to-Frequency Mappings
USA/FCC & Canada regions have 11 total channels allocated.
All frequencies are in GHz.
Channel Lower Center Upper Frequency
1 2.401 2.412 2.423
2 2.404 2.417 2.428
3 2.411 2.422 2.433
4 2.416 2.427 2.438
5 2.421 2.432 2.443
6 2.426 2.437 2.448
7 2.431 2.442 2.453
8 2.436 2.447 2.458
9 2.441 2.452 2.463
10 2.446 2.457 2.468
11 2.451 2.462 2.473

## Slide 5: Why not use a normal spectrum analyzer?
Big and heavy
Big and expensive
Overkill in a lot of cases
Handheld 2.4 GHz spectrum analyzers available, but very expensive

## Slide 6: So what is this Proxim 7400 thingy?
It’s an obsolete, pre-802.11 wireless networking card, circa 1999
It supports Frequency Hopping Spread Spectrum (FHSS)
FHSS uses 80 1 MHz-spaced channels, from 2401 to 2480 MHz
Each FHSS session frequency hops across 15 of these channels

## Slide 7: So why are you trying to sell me on this obsolete junk?
Because, the Proxim 7400 software includes a ‘Snoop’ application that scans the spectrum from 2401 to 2480 in 1 MHz steps and graphically displays the signals it receives.
In essence, a crude spectrum analyzer that can be used to display the 2.4 GHz ISM band

## Slide 8: Like this

## Slide 9: 2.4 GHz cordless phone

## Slide 10: Wireless AP on channel 6

## Slide 11: Wireless AP on channel 11

## Slide 12: 5 feet from microwave oven on high

## Slide 13: The skinny
PCMCIA card
Drivers available from Proxim website for Win 2000, Win ME, Win 98, Win 95, Win CE
No driver available for Windows XP
On sale for $20 - $40 on eBay, Yahoo
Removable dipole antenna; some cards sold with a second antenna

## Slide 14: The card

## Slide 15: MMCX jack