## Slide 1: Building Cavity Filters
N5PYK
November 2003

## Slide 2: Parts needed for VHF cavity
12” long 2” copper pipe
2 2” pipe endcaps
11” ½” copper pipe
2 BNC connectors
8” of #14 wire
¼” brass nut
12” of ¼” allthread
7 ¼” nuts
1 nylon spacer to just fit inside the ½” pipe
8 2-56 screws
8 2-56 nuts
2” ¼” stainless screw

## Slide 3: Mounting of connectors
Drill 3/8” holes on opposite sides of 2” pipe 2” from bottom
Drill smaller mounting holes for securing connector w/ 2-56 screws
Fasten connectors with screws and nuts

## Slide 4: Soldering center conductor
Ensure ½” pipe is cut squarely and shine with scotchbrite or steel wool
Center the ½” pipe in the 2” endcap
Solder pipe to endcap with propane torch.

## Slide 5: Two pieces done!

## Slide 6: Top endcap prep
Drill 3/8” hole in center of second endcap
Place stainless screw in nut to ensure nut does not move when soldering.

## Slide 7: Solder brass nut to endcap
Using propane torch solder the brass nut to the endcap then remove stainless screw

## Slide 8: Build coupling loop
Cut #14 wire to make
Two pieces as shown.
Dimensions optimized
Left rise ½”
Length 2”
Right rise ¼”

## Slide 9: Install coupling loops
Solder short end of wire to center conductor of connector
Then, using propane torch, solder longer end to 2” pipe as near to the bottom as you can without spilling solder to the outside of the pipe
Then, reflow solder on connector to ensure good connection
Insertion loss and Q of cavity is modified by bending loop toward or away from ½” pipe
Less insertion loss = lower Q (tighter coupling)

## Slide 10: Endcap tuning piston
Insert allthread into
Top pipe cap
Put spacer on allthread near left side and secure with 2 nuts on either side of spacer
Use one nut to tighten rod to brass nut after frequency set
Make adjustment knob by putting two nuts together
Solder top endcap to 2” pipe—Secure bottom endcap with screws

## Slide 11: Finished product
Thus far, haven’t seen need to solder bottom
Endcap which allows user to adjust Q/IL
Prototype had 4.5 MHz bandwidth at 160Mhz
With 0.2dB insertion loss.
Adjust insertion loss with proximity of loops to ½” center conductor in cavity. Loops can not touch the copper center conductor.
Tune cavity with all-thread. Screw in=lower frequency. Out=higher frequency
Prototype tuning range: ~170Mhz to ~108 MHz