## Slide 1: Dallas Area HSMM Update March 10, 2004
W5HN
North
Texas
Microwave
Society
NTMS
John Beadles - N5OOM
North Texas Microwave Society

## Slide 2: Dallas Area HSMM Activity
HSMM applications identified
DAWG HSMM Merging into NTMS
NT5NT access point in operation
Coordination with national activities
Ham IP subnet sought
Public service events
Evangelism, training activities
Metropolitan area network planning
Emcomm access point development

## Slide 3: HSMM Applications
Hospital / EOC interconnects
Document Storage & Access
Printer Sharing
IRLP Repeater Links
APRS Internet Feed
Local Event Management
Internet-based Weather Services
Regular Internet Service

## Slide 4: DAWG HSMM merging with NTMS
N5PYK investigates NTMS interest in HSMM, finds widespread acceptance
N5OOM investigates DAWG-HSMM interest in merging with NTMS, finds acceptance, no negative responses
HSMM activities presented at Mar 6 NTMS meeting
DAWG HSMM to discuss at

## Slide 5: NT5NT Test AP in Operation
Currently a repackaged Linksys WAP11
Users need a fixed IP, must register MAC addr
16 db hpol panel antenna pointing north toward McKinney
No inherent internet access, can only provide a bridge between clients
Current reception reports
  N5OOM received at 190 & Plano Rd (1.9 mi) with 5db ant
  N5PYK did not receive in McKinney w 24 db grid
Need to re-point antenna to support Richardson “Wild Ride” bike rally

## Slide 6: Coordination with National Activities
ARRL HSMM working group notified of local activities
National WG seeking volunteers for task groups
  HSMM applications working group
  Radio Metro Area Network working group
  Software development working group
  Seeking product reviews for QST or QEX
  Installation of AP at W1AW

## Slide 7: IP Subnet Sought
Clear that we’re going to have an RMAN, we’ll need a ham subnet
Found list of national AMPERNET coordinators, but no obvious NTX coordinator
Following up with investigation
Need to determine how we’d structure an RMAN network (one big subnet, or route between area subnets )

## Slide 8: Public Service Activites
Richardson “Wild Ride” Bike Rally
  May 8
  Starts near Nortel, goes to Lake Lavon
  Want to cover Start /Stop and 3 rest stops
  Combination of direct coverage from Nortel AP, remote Internet links
Collin Classic Bike Rally
  June 12
  Short distance link between net control area with event logistics coordinator
  Provide APRS-IS, custom web app
Plano Balloon Festival
  Late September
  Cover launch field, recovery team areas
Others?

## Slide 9: Evangelism, Training
DAWG-HSMM meetings publicized by NTX Section Manager
Need to push out to area clubs
Must create a set of introductory user writeups
  Types of HSMM equipment
  How to buy an access point
  Differences between Part 97, part 15 operation
Hamcom presentations
Currently 9 HSMM presentations, including basic HSMM, TCP/IP networking & networking security

## Slide 10: Metropolitan Area Network
HSMM working group to investigate the creation of a Metropolitan Area Network
Should be designed as an alternative to landline based internet in the event of a major area outage
Need to find a high reliability internet feed
  Maybe a link to local SWB or MCI facility
  Directway satellite as an emergency alternative
Would have to bring in local area clubs, RACES & ARES orgs who would have to contribute, provide maintenance
Investigate benefits of Part 15 vs Part 97 operation
Benefit in partering with local WISP operators to extend network?
Provide wireless internet service to area Hams by structuring network as a co-op?

## Slide 11: EMCOMM AP Development
I’m intending to build an emergency deployment access point to take to EMCOMM events.
Got tagged to be the staging site coordinator for Collin County ARES, so I have a proprietary interest in getting this done
Intent the system to support staging site activities
Will structure so as to support public service events as well (good testing)

## Slide 12: EMCOMM Access Point
Net Controls
Served Agency Liasons
Weather Liasons
Health & Welfare Liasons
Access Point for
Local Distribution
Bridge to an internet connection
DSL Router
Laptop configured as an EMCOMM Server
Equipment in weatherproof boxes
Power run up the Ethernet cable

## Slide 13: EMCOMM Server
Kit will include a prepackaged Laptop
Linux (or other Unix) installation with
Web server
  Web forums package (w email link)
  Custom web app for managing volunteers, deployment locations, logistics, schedules
  Store ICS forms
  Area maps
  APRS web server, internet feed
FTP server
  Allow access to files
SMTP eMail server
Instant messaging
Need a lightweight DNS server
Need to figure out how to centralize web management for all of these features

## Slide 14: EMCOMM AP Hardware
Kit to provide enough eqpt to establish a local area coverage network
DSL router (provide for link back to internet)
AP to cover local area
Bridge back to local area
May have additional equipment to extend network to other locations, larger area coverage
Powerline networking eqpt?

## Slide 15: 900MHz ISM Band WLAN
No 802.11 standard
Vendor proprietary chanellizations
DSSS and FHSS methods
Some tree penetration capability
100 Kbps to 2 Mbps bandwidth

## Slide 16
2.4 GHz (802.11b/g)
802.11b channels 1-6 overlap amateur allocations
AMSAT requests not to use ch 1 due to sat interference
11 overlapping 802.11b/g channels
11 MHz wide each, 5 MHz spacing

## Slide 17
5 GHz (802.11a)
12 non-overlapping 802.11a channels
20 MHz wide each
3 sets of 4 channels
  4x40mw ch for indoor
  4x200mw ch for indoor, outdoor
  4x800mw ch for outdoor
  Power specified at the IR
More bandwidth requested