## Slide 1: Antenna Aiming Issues for Rovers
By
Wes Atchison
WA5TKU

## Slide 2: Antenna Aiming Issues for Rovers
Short Distance 6 Digit Grid Square Point
Compass Correction
GPS
Dish Aiming
Summary
References

## Slide 3: 6 Digit Point Error
4 Miles
3 Miles

## Slide 4: 6 Digit Point Error

## Slide 5: 6 Digit Point Error
Assume 36 inch Dish:
Beam Width ~ 2.5 Degrees
X = 2 / Tan 2.5
Minimum Distance Between Stations = 45.8 Miles

## Slide 6: 6 Digit Point Error
Points to Ponder
  Be Aware of Close in Error
  Could Be Cause of Missed Close in Contacts
  Use Knowledge of Area
  Use Lat/Long

## Slide 7: Compass
Compass Error
  Magnetic Variation/Declination
    Magnetic North and True North Not Same
    Error Varies with Location on Earth with Respect to Magnetic North
    Changes with Time
  Magnetic Deviation
    Varies with Surrounding Magnetic Fields

## Slide 8: Compass
Magnetic Variation/Declination

## Slide 9: Compass
Variation Changes with Time
  Map Contour Minutes/Year

## Slide 10: Compass
Can Dead Men Vote Twice At Elections
  Compass
  Deviation
  Magnetic
  Variation (Declination)
  True
  Add
  Easterly

## Slide 11: Compass
Compass
  Uncorrected Heading Read Off the Compass
Deviation
  Affects of Unknown Magnetic Fields
    Automobile
    Power Lines
    Iron Deposits

## Slide 12: Compass
Variation (Declination)
  Affect of Magnetic North and True North Not in Same Location
  Varies with Location on Earth
  Correction is in Terms of East or West
  Correction Changes with Time

## Slide 13: Compass
True
  Heading with Deviation and Variation Correction Applied
  Referenced to True North
Add
Easterly Corrections From Compass To True

## Slide 14: Compass
Confusion
  Start With True From Computer Program
  Easterly Errors Must be Subtracted When Changing from True to Compass
  Deviation is Unknown Use 0 Correction

## Slide 15: GPS
GPS
  Location
  Calculated Direction
  Displays Direction IF Moving
  Operates from Batteries
  Unfamiliar with Functions

## Slide 16: Dish Aiming Tools
Dish Aiming
  Compass
  Compass Rose
  Beacons
  Know Station
  Landmarks

## Slide 17: Dish Aiming Tools
Compass
  Correct for Magnetic Errors
  Move Away from Automobile
  Site Object on Horizon with Compass in Direction of Interest
  Aim Dish at Objected Sited on Horizon

## Slide 18: Dish Aiming Tools
Compass Rose
  Circle Marked in Degrees
  Adjustable Around Mast
  Pointer on Mast
  Set with Compass
  Set to Station Worked
  Set to Beacon
  Set to Landmark

## Slide 19: Dish Aiming Tools
Maps
  USGS
    Out of Date
  Aircraft Sectional
    Updated Regularly
  Map CDs
    Made from USGS Data – Question Data
  Road Maps
    Look for Lat/Long Marks

## Slide 20: Summary
Tools
  Know How to Use
  Practice Usage
  Knowledge of Limitations
  If Possible Visit Site

## Slide 21: Antenna Aiming Issues for Rovers
References:
  http://www.learn-orienteering.org/old/
  http://www.thecompassstore.com/whatisdec.html
  http://geomag.usgs.gov/faq.html
  http://geology.isu.edu/geostac/Field_Exercise/topomaps/bearing.htm
  http://www.tpub.com/content/administration/14220/css/14220_69.htm