## Slide 1: Introduction to the Linksys WRT-54G
W5HN
North
Texas
Microwave
Society
NTMS
John Beadles – N5OOM
North Texas Microwave Society
January 3, 2005

## Slide 2: John, what the heck are you doing and why should we care?
I want to provide a failure resistant wireless backbone for metropolitan area ham digital systems
  Echolink
  IRLP
  Winlink2k
  APRS
  Telpac
  Repeater control
Benefits
  Will make internet access more resistant to failure of local internet service
  Help spread the cost of internet access across multiple clubs, individuals, organizations

## Slide 3: Digital Network Example

## Slide 4: How does the Linksys WRT-54g fit in?
The Linksys WRT-54g turns out to be easily modifyable with firmware and hardware extensions
The device uses Linux based firmware and can be flashed with customized versions
3rd party firmware allows the xmit power to be increased, sometimes substantially
The 3rd party firmware also provides for WDS bridging

## Slide 5: Basic Information
From www.seattlewireless.net
TX Pwr
  31mw out of box
  Can be upgraded to 84mw in software
  Reports of 250mw using Sveasoft “Alchemy” firmware
  But beware of unconfirmed reports of overheating issues
Receive Sensitivity (unconfirmed)
  -65dbm running 802.11g 54mb
  -80dbm running 802.11b 11mb
DC Power
  V1.0? – 5v @ 2a
  V2.0 – 12v @ 1a (internally regulated down to 3.3v)
  Voltage regulation on the v2.0s is reported to be done by an AnaChip 1501-33, a 150KHz, 3A DC-DC converter with a 45v max imput voltage. This might permit the direct use of 24v or (almost) 48v POE supplies

## Slide 6: Hardware
From www.seattlewireless.net
CPU
  v1.x Broadcom BCM4702KPB – 125MHz
  v2 – Broadcom BCM4712KPB – 200MHz
Flash
  v1.x - AMD AM29LV320DB-90EI (32Mbit)
  v2 – Intel TE28F320 C3 flash 32Mbit
RAM
  2x IC42S164000 (64Mbit or 4Mx16) Ram Chips
Ethernet
Wireless
  v1.0 – Mini PCI Linksys / Broadcom w dual Hirose connectors
  v1.1 – Integrated onto motherboard
  v2 – Integrated Broadcom BCM2050KWL

## Slide 7: External Pictures
Pics snarfed from seattlewireless.net

## Slide 8: V1.0 Internal Pictures
Pics snarfed from seattlewireless.net

## Slide 9: Hardware & Software Versions
Firmware
  1.01.4 – Linux kernel 2.4.5, broken WPA security
  1.02.1 – 802.1g standard updates
  1.30.1 – 802.11g standard compliance
  1.30.7 - Fixes
  1.41.2 – Changed web layout
  1.42.2 – Linux kernel 2.4.20, other fixes
  1.42.3 - Fixes
  2.00.8 – Updated wireless driver
  2.02.2 – Repeater support
  2.04.3 – Numerous added features
  2.04.4 – Updated wireless driver
  3.01.3 – Supports v2.2 hdwr
Hardware
  WRT-54Gv1.0 – 5v w separate wireless
  WRT-54Gv1.1 – 12v with integrated wireless
  WRT-54Gv2.0 – More chipset integration
  WRT-54Gv2.2 – Updated ethernet controller?
  WRT-54GSv1.0 – Speedbooster - More ram & flash
3rd Party Firmware
  Sveasoft
    http://www.sveasoft.com/
    Many unix commands and RF control
    Support by subscription
  HyperWRT
    http://www.hyperdrive.be/hyperwrt
    Stays close to original firmware but with added features
  Wi-fi Box
    http://wifi-box.sourceforge.net/
  Ewrt
    http://www.portless.net
    Provides a captive portal based on NoCatSplash
  Batbox
    http://www.batbox.org/wrt54g-linux.html
    Adds misc unix tools for box exploration purposes
  OpenWRT
    http://openwrt.org/
    Minimal firmware with support for add-ons

## Slide 10: Internal Architecture
From seattlewireless.net
Note that the wireless segment is separate from the local lan segment

## Slide 11: Wireless Distribution System
Access Point and Client modes are built into the 802.11x specification, which limits how units can be connected together
WDS is used to provide greater flexibility in linking wireless nodes
  Are MAC address based
  And use a special data frame that uses up to 4 MAC addresses in a frame rather than usual 3
Interoperability is not guaranteed
  Implementations may vary from vendor to vendor
  But many products are based on the Broadcom chipset so may be compatible
Bridge mode
  Acts as a wired ethernet bridge between one or more APs
  APs talk only to each other, clients are not allowed
Repeater mode
  Provides connections between both APs and clients
  Reduces system throughput since radio is having to handle traffic both between clients and remote AP
See also:
  http://www.smallnetbuilder.com/Sections-article78-page1.php for details
  http://www.proxim.com/support/techbulletins/TB-046.pdf

## Slide 12: WDS Configuration
Assign a static IPs
  For simplicity stay in the same subnet for all APs and clients
Collect the wireless MAC address for each AP
  Write down a table of the wireless MAC address and the IP address for each AP
  Note that some units have separate MAC addresses for the WAN port, the wired ethernet ports and the wireless port. For this you want the wireless port.
Verify that your client can connect to each AP
Set all APs to same clear frequency
Set SSIDs on each AP
  WDS is MAC level bridging and does not care about SSID
  If your clients are mobile, APs should all share same SSID so that clients will roam across APs
  For testing, may want to set different SSIDs so that you can see what you are connecting to, but then you will have to connect to them automatically.

## Slide 13: ID with WDS
If the AP function is left running on each WDS bridged unit, this serves to act as a legal ID
Clients still need to have some ID method, but if clients are hardwired to a bridge, this is is avoided.
Need to see how to lock clients out while leaving the SSID broadcasting.

## Slide 14: Tested 2 Hop WDS Bridge
Ethernet cable from switch port to switch port
All APs broadcasting call based SSID
PC client connection tested to each unit

## Slide 15: Tested 3 Hop WDS Bridge
All APs broadcasting call based SSID
PC client connection tested to each unit

## Slide 16: Info Sources
http://www.linksys.com/
  Factory support
www.wrt54g.com
www.seattlewireless.net
  Rather a lot of technical and programming info.
www.linksysinfo.org
  3rd party info on a range of Linksys products
forums.wirelessnederland.nl
  Multiple languages, but technical discussions
Broadband Reports Linksys Forum
  http://www.broadbandreports.com/forum/linksys
Modified WiFi for Ham radio
  http://www.qsl.net/kb9mwr/projects/wireless/modify.html
  http://www.qsl.net/n9zia/wireless/index.html