## Slide 1: LDO noise effects – part 1 July 1, 2023 KM5PO & KI5EMN

## Slide 2: “Noise” is everywhere
Noise is an unwanted disturbance in an electrical signal
Noise generated by electronic devices varies greatly as it is produced by several different effects.
In particular, noise is inherent in physics and central to thermodynamics. Any conductor with electrical resistance will generate thermal noise inherently. The final elimination of thermal noise in electronics can only be achieved cryogenically, and even then quantum noise would remain inherent.

## Slide 3: “Noise” types
Thermal generated by the random thermal motion of charge carriers (usually electrons), inside an electrical conductor, which happens regardless of any applied voltage
Shot random statistical fluctuations of the electric current when the charge carriers (such as electrons) traverse a gap. If electrons flow across a barrier, then they have discrete arrival times
Partition where current divides between two (or more) paths
Flicker a signal or process with a frequency spectrum that falls off steadily into the higher frequencies
Burst sudden step-like transitions between two or more discrete voltage or current levels
Transit-time If the time taken by the electrons to travel from emitter to collector in a transistor becomes comparable to the period of the signal being amplified
Coupled
    can be coupled into a circuit from the external environment, by inductive coupling or capacitive coupling, or through an antenna..
    Intermod/Crosstalk/Interference/Atmospheric/Industrial/Solar

## Slide 4: Mitigation
Faraday cage – A Faraday cage enclosing a circuit can be used to isolate the circuit from external noise sources. A Faraday cage cannot address noise sources that originate in the circuit itself or those carried in on its inputs, including the power supply.
Capacitive coupling – Capacitive coupling allows an AC signal from one part of the circuit to be picked up in another part through the interaction of electric fields. Where coupling is unintended, the effects can be addressed through improved circuit layout and grounding.
Ground loops – When grounding a circuit, it is important to avoid ground loops. Ground loops occur when there is a voltage difference between two ground connections. A good way to fix this is to bring all the ground wires to the same potential in a ground bus.

## Slide 5: Mitigation
Shielding cables – A shielded cable can be thought of as a Faraday cage for wiring and can protect the wires from unwanted noise in a sensitive circuit. The shield must be grounded to be effective. Grounding the shield at only one end can avoid a ground loop on the shield.
Twisted pair wiring – Twisting wires in a circuit will reduce electromagnetic noise. Twisting the wires decreases the loop size in which a magnetic field can run through to produce a current between the wires. Small loops may exist between wires twisted together, but the magnetic field going through these loops induces a current flowing in opposite directions in alternate loops on each wire and so there is no net noise current.
Notch filters – Notch filters or band-rejection filters are useful for eliminating a specific noise frequency. For example, power lines within a building run at 50 or 60 Hz line frequency. A sensitive circuit will pick up this frequency as noise. A notch filter tuned to the line frequency can remove the noise.

## Slide 6: LDO PSRR vs other noise
Power Supply Rejection Ratio (PSRR)
Is a measure of circuit’s power supply rejection expressed as a ratio of output noise to noise at the power supply input – is a function of frequency/affected by the gain bandwidth of the EA/load current variation has impacts
PSRR = 20 log ( Ripple input divided by Ripple output )
Other LDO noise
Noise generated by the transistors and resistors in the LDO’s internal circuitry (thermal, flicker, shot) and by the external components

## Slide 7: In the shop
Mats referred me to the Sparkos LDO

## Slide 8: In the shop
In the datasheet

## Slide 9: In the shop
In the datasheet

## Slide 10: In the shop
Noise measuring setup

## Slide 11: In the shop
Protection for soundcard

## Slide 12: In the shop
Ready to measure

## Slide 13: Noise measures
Calibrated system – laptop powered 6-10-23
Measurement of 1 Khz at .001v (1 mV) in the tin can
Calibrated system – laptop powered 6-10-23
Measurement of 1 Khz at .001v (1 mV) in the tin can

## Slide 14: Noise measures
Calibrated system – laptop powered 6-10-23
Measurement of 51 ohm resistor in the tin can
12 uV of ripple at 60 hz

## Slide 15: Noise measures
Calibrated system – laptop on battery 6-10-23
Measurement of 51 ohm resistor in the tin can
Peak of 1.74 uV < 20 KHz ~280 nV average noise < 20 Khz

## Slide 16: Noise measures
Calibrated system – laptop on battery 6-10-23
Measurement of 51 ohm resistor in the tin can
Peak of 1.74 uV < 20 KHz ~280 nV average noise < 20 Khz

## Slide 17: Noise measures
LM317 number 1 breadboarded circuit (12 vDC in – 5 vDC out – 51 ohm load - 75 mA draw) ~ 5-7 uV peaks below 2 khz, broad peak of 15 uV on 5 KHz, 10 mV spike at 35 Khz
.003 % of 5v=15 uV

## Slide 18: Noise measures
MH-MINI-360 (12 vDC in – 5 vDC out – 51 ohm load) ~6 to 10 uV peaks <500 Hz, rising noise of 10 to 40 uV at 20 KHz, peak of ~ 1 mV at 12 KHz

## Slide 19: Noise measures
Sparkos lab SS7805 (12 vDC in – 5 vDC out – 51 ohm load - 120 mA draw) ~ 4 uV peak at 120 hz otherwise < 3 uV from 50 hz to 20 khz and 5 mV spike at 35 khz

## Slide 20: Noise measures
DigiLO wal wart power supply 100 mV ripple at 120 hz

## Slide 21: Spectrum effects
DigiLO output spectrum

## Slide 22: Spectrum effects
DigiLO output spectrum

## Slide 23: Noise measures
iPhone charger (120vAC in 5.0 vDC out) 1 mV spike at 35 KHz

## Slide 24: Noise measures
“Switcher power supply” (120vAC in 6.0 vDC out) I was using back in 2008 to drive a T/R relay for 1296 MHz

## Slide 25: Noise measures
Buck converter XL4016E1 number 1 (12vDC in – 5.0vDC out – 100 ohm load – 50 mA draw) ~40 uV < 20 Khz, broad 100+ uV spike at 43.2 Khz, 11 mV spike at 35

## Slide 26: Spectrum effects
Wavelab 1819 MHz LO - McCoy 10 MHz OCXO (12 vDC) sharing PDU with 24 GHz system (uses XL4016 buck conv) – spur is -37 ~+184 KHz

## Slide 27: Spectrum effects
Wavelab 1819 MHz LO - 5v 10 MHz OCXO powered by Sparkos LDO sharing PDU with 24 GHz system (uses XL4016 buck conv) – spur is negligible

## Slide 28: Focus testing

## Slide 29: Focus testing

## Slide 30: Focus testing

## Slide 31: Focus testing

## Slide 32: Focus testing

## Slide 33: Focus testing – 50 KHz span

## Slide 34: Focus testing

## Slide 35: Focus testing

## Slide 36: Focus testing

## Slide 37: Next steps – to be continued
Spectral Noise density curve and a rising noise floor for RF apps
Effects on ADC or DAC. Sampling system causes high frequency noise to fold to lower frequencies due to aliasing
Reducing LDO noise-
  Understanding the datasheet
  Use best LDO you can afford
  Cascade multiple LDOs

## Slide 38: Questions?