## Slide 1: A 10 GHz repeater using junk box components
Gary Lauterbach AD6FP

## Slide 2: Acknowledgements
Kerry N6IZW
  San Diego ONCAR 1997
  Wide band, 100 db gain
Dave WW2R
  IDer and DTMF decoder SW
Parts and help:
  Lars AA6IW
  Rex KK6MK

## Slide 3: Goals
Promote 10 GHz activity by providing a common line-of-site point between club members
Put it together quickly with parts on hand

## Slide 5: Block Diagram

## Slide 6: LO Scheme
Crystals on-hand dictated odd LO frequencies
118 MHz first IF allows good image and LO rejection
10.7 MHz IF allows common filters
Input: 10368.575 +/- 22 KHz
Output: 10369.175 +/- 22 KHz
Beacon: 10369.150

## Slide 7: System Gain
Noise in 44 KHz BW:
  1.7*10^-16 watt, 3db NF
  -127 dbm
Repeater gain set to 3 dbm noise output: 130 db gain
System gain with antennas 150 db

## Slide 8: Block Diagram

## Slide 10: Beacon / ID
At bottom edge of passband
Set to 17 dbm output level, 10db below maximum output
CW ID: call and grid square every 90 seconds
Two active parts:
  PIC 16F84 and NE602

## Slide 11: Control Link
Commercial 440 FM receiver and DTMF decoder control:
  Transmit On/Off
  Receive On/Off
  High/Low power
  Translating/Non-translating
  High/Low gain

## Slide 12: Antennas
Two waveguide slot antennas:
  11’ vertical distance between xmit & rcv antennas
  16 slots, 10 db gain
W1GHZ spreadsheet used to calculate slot spacing/offset
  Taylor amplitude distribution
“Wings” for more uniform pattern

## Slide 15: Long Path Calculation
K7NOM to repeater:
  111Km: 157 db path loss
  -113 dbm for full output
  157 – 113 = 44 dbm erp (20 mw and 18” dish)
Repeater to K7NOM:
  37 dbm erp – 157 = -120 dbm
  2.4 KHz BW, 3 db NF = -140 dbm
  20 db s/n with isotropic antenna

## Slide 16: Short Path Calculation
AD6FP to repeater:
  142 db path loss
  142 –113 = 29 dbm erp (100 mw and 16 slot omni)
Repeater to AD6FP:
  37 dbm – 142 = -105 dbm
  2.4 KHz, 3 db NF = -140 dbm
  35 db s/n with isotropic antenna

## Slide 17: Installation
Mt. Allison, Fremont California
  CM97BL, 2658’ ASL
Installation Team:
  K6GSJ, WT6K, AA6IW,W6QI, KD6BPP

## Slide 19: Radio Mobile Coverage Plot

## Slide 20: Summary
Successfully promotes activity
  Weekly microwave net
  Resource for rig testing
Will be available world-wide through Echo-Link