## Slide 1: SSETI Express satellite mode S data and voice transmitter
Presented by Sam Jewell, G4DDK

## Slide 2: CONTENT
Introduction to SSETI
Why and how are we involved?
The S band package
The S Band modulator
Acknowledgements

## Slide 3: What is SSETI?
Student Space Exploration and Technology Initiative
Students from twelve different European countries are participating in SSETI. They are building the first pan-European student satellites together. They are all united by their desire to 'launch the dream‘.

## Slide 4: Who is behind SSETI?
ESTEC
  European Space Research and Technology Centre (Noordwijk, The Netherlands)
  Educational outreach arm of:
ESA
  European Space Agency

## Slide 5: What is SSETI planning?
Mission 0: Sseti Express is planned to be launched in Low Earth Orbit in early 2005. the satellite should serve as a technological demonstration and as a test bed for some of the hardware that will be used for ESEO.
Mission 1: The European Student Earth Orbiter (ESEO) should be launched directly into an geo-stationary transfer orbit using an Ariane 5 launch vehicle. - planned for end 2005
Mission 2: After the first mission has succeeded, the next step will be the development of a Moon Orbiter to prepare a final Moon landing.
Mission 3: The last step is the final Moon landing. This includes to drop a Moon Rover which will explore the Moon.

## Slide 6: Why and how are we involved?
To create a network of students, educational institutions and organisations (via the internet) to perform the distributed design, construction and launch of (micro)-satellites and other spacecraft is the main objective of the SSETI initiative.

## Slide 7: SSETI Express
The SSETI Express mission is an educational mission that shall deploy CUBESAT pico-satellites developed by universities, take pictures of Earth, act as a test-bed and technology demonstration for hardware of the complementary project: the European Student Earth Orbiter, and function as an radio transponder for the rest of it’s mission duration"

## Slide 8: SSETI Express

## Slide 9: SSETI Express passengers
XI-V from Japan, University of Tokyo
UWE-1 from Germany, University of Würzburg
Ncube-2 from Norway, Andoya Rocket Range They will be deployed from a T-Pod developed by UTIAS Space Flight Laboratory, Toronto

## Slide 10: SSETI Express payload

## Slide 11: SSETI Express parameters
The satellite is approximately 60*60*70cm and weighs 80kg SSETI Express is planned to fly on the DMC-3 Cosmos launch vehicle from Plesetsk in Russia. The main passengers of this launch are two commercial satellites from Surrey Satellite Technologies Limited (SSTL), United Kingdom. Launch is planned April 2005 by Polyot in Plesetsk The orbit is circular SSO : 686km, 98.3deg 11:00AM LTAN The period of the orbit is around 90min

## Slide 12: SSETI Express communications
Primary communications will be simplex 9.6kb/s on 437MHz using a specially qualified T7F transceiver produced by Holger Eckart, DF2FQ

## Slide 13: The S Band package
Consists of
3W, 2401.840MHz single channel, directly modulated FM transmitter.
TNC7
SMPSU
Logic and interface board
Sensor board
3-way antenna splitter

## Slide 14: S Band modes
Data or voice configuration
Data
  38.4kbit/s from the TNC7. Relays satellite experiment data and camera data stream
Voice
  Relay of the 437MHz voice uplink
    CTCSS enabled
    DTMF-based telemetry frame every 2 minutes*

## Slide 15: SSETI Express S band test bed

## Slide 16: The S Band Transmitter
Express – 6 weeks to produce a working prototype.
  Direct FM modulation using ‘G3RUH’ data stream shaping (filtering)
  Existing, flight proven (ECHO) PA from G3WDG
  PA monitoring for power output, heatsink temperature and supply current (maybe RSSI)

## Slide 17: The S Band Transmitter
Tight spectral mask – lots of filtering.
12kHz peak deviation with high linearity for data
5kHz peak deviation for voice and DTMF telemetry
Low current consumption <10W for the entire module.

## Slide 18: The S Band Modulator
300MHz
multiplier
2400MHz
multiplier
De-emphasis
cct
Butler - FET
1200MHz
multiplier
Driver
amplifier
Unswitched 8V
Switched 8V
PA

## Slide 19: The S Band modulator

## Slide 20: S Band modulator de-emphasis

## Slide 21: The prototype RF deck

## Slide 22: Spectral purity

## Slide 23: FM Deviation

## Slide 24: S Band module logic side

## Slide 25: Acknowledgements
Jason Flynn, G7OCD
Graham Shirville, G3VZV
David Bowman, G0MRF
Howard Long, G6LVB
Charlie Suckling, G3WDG
University of Wroclaw, Poland
Amsat-UK
SSTL
ESTEC

## Slide 26: David

## Slide 27: Jason

## Slide 28: Thankyou!
Sam Jewell, G4DDK
jewell@btinternet.com
g4ddk@hotmail.com
www.btinternet.com/~jewell