## Slide 1: Simplified DDS/PLL Software Development for Microwave Synthesizers
John Miles, KE5FX

## Slide 2: Introduction
- Who am I?
- “Beware of programmers with screwdrivers.”
-- Robert Roy W4PZA
- What projects inspired me to research this topic?
- DC - 1 GHz general coverage receiver
- Uses two ATmega128 controllers and one Mini-ITX PC motherboard
- Lots of register-level programming!
- Wanted a general-purpose way to build and work with homebrew microwave signal sources

## Slide 3: Focus on CW sources
Rx / Tx LOs
Homebrew signal sources for test equipment
Slow-speed OOK/FSK applications
  Modulate input reference within loop bandwidth
  Beacons
High-speed FM/FSK applications with no low-frequency components near the loop bandwidth
  Add modulation directly to VCO tuning line

## Slide 4: Quick overview of hybrid DDS/PLL architecture
DDS as PLL reference
  AD9852/4
Post-DDS filtering
Programmable PLL IC
  ADF411x family
  LMX23x6 family
VCO
Loop filter
Control platform

## Slide 5: DDS as Reference
PLL reference is typically, but not necessarily, a fixed source
In a hybrid PLL synth, the DDS is the “reference”
Above diagram from Analog Devices AD9850 data sheet
AD9852/54 is more complex, but we don’t use most of its features

## Slide 6: DDS as Reference
Single-loop PLLs normally tune in steps determined by N * comparison frequency
Slight change in reference frequency can fill in the gaps between PLL multiplication steps (N factors)
DDS technology is ideal for this
  Very simple way to achieve high tuning precision without multiple loops
  Typically capable of much better precision than most applications need

## Slide 7: DDS as Reference
Drawbacks to DDS reference include spurs
  In-band spurs are multiplied by 20*log(N)!
  Out-of-band spurs can still cause EMI/crossmod problems
  Higher-precision DAC (14 bits) offered by AD9852/AD9854 delivers better SFDR, but...
  Post-DDS filtering is still a must
No need for exotic DDS parts
  Reference generated at 10.7 MHz
  Low-current parts are better if you have a choice
    Less likely to cause RFI problems

## Slide 8: Post-DDS Filtering
Monolithic crystal filter
  ECS-10.7-15B (+/- 7.5 kHz bandwidth, 25 kHz stopband) is a good choice
  Inexpensive, available from Digi-Key as X704-ND
  Matching not critical -- comparator will take care of ripple

## Slide 9: Post-DDS Filtering
LC low-pass filter
  We use a three-pole design with 12 MHz cutoff
  Eliminates higher-order DDS images that pass through the crystal filter and cause spurs in PLL output even though they’re far outside the loop bandwidth
Comparator
  AD9852/9854 has its own built-in comparator, but it’s not optimal
    3.3V operation, but PLL chips work best with near-rail-to-rail 5V input
    Some users have observed poor noise/jitter performance
  We use an LT1016 high-performance 5V comparator
    Good to near 100 MHz

## Slide 10: PLL Device Selection
Many parts available
  Analog Devices ADF411x family
    ADF4110-ADF4113: 5V parts for 550 MHz - 4 GHz
    ADF4106-ADF4107: 3.3V parts for 6-7 GHz
  National Semiconductor LMX23x6 family
    Lower frequency limits than ADF series
    Fewer programming options
Don’t overspecify the frequency limit if possible
  Bathtub-shaped sensitivity graph can lead to harmonic-locking problems
  Higher-frequency parts are more expensive

## Slide 11: PLL Device Architecture
Above diagram from National Semiconductor LMX2326 data sheet
  Also applies to ADF411x parts with very few differences
All National/Analog PLL devices use 3-wire serial programming
  ADF411x PLLs use 24-bit words
  LMX23x6 PLLs use 21-bit words
AD9852/4 DDS also uses 3-wire programming (8-bit words)
  Same basic interface circuitry and programming code for all PLL/DDS parts

## Slide 12: Control Platform Choices
PC
  Good for ambitious projects with lots of user interface code
    Built-in video, networking, audio hardware, etc.
    Support for almost any programming language in existence
    PC CPUs are capable of very high DSP performance
    High-end equipment from Tektronix, Agilent, etc. is based on Windows PCs these days(!)
      Very neat to have same resources available to Amateur experimenters
  Good development/test platform
    Use parallel or USB port(s) to talk to DDS, PLL, other chips
    Use serial port(s) to talk to microcontrollers
    Note that direct access to parallel port under NT-based versions of Windows requires some extra work
      http://www.beyondlogic.org/porttalk/porttalk.htm

## Slide 13: Control Platform Choices
PC (continued)
  Windows PCs are usually not a good choice for “hard realtime” control
    Better to delegate realtime work to dedicated controllers
    Linux/BSD may be a possibility as well
  Historically not a good choice for small projects due to space/power requirement, but new form factors like Mini-ITX are changing that!

## Slide 14: Control Platform Choices
Atmel AVR / ATmega
  Fantastic choice for small-scale projects
    Lots of built-in I/O
      Parallel
      Serial
      ADC channels
    Low power consumption
    Hard realtime performance
      Total control over interrupts, timers, CPU cycles...
    Healthy developer community (www.avrfreaks.net)
  Almost code-compatible with PC C++, thanks to AVR-GCC!
  Lots of prototyping resources available
    Example: ATmega128 board from www.bdmicro.com
    128K Flash memory
    4K RAM
    16 MHz

## Slide 15: Control Platform Choices
Hybrid approach best for complex projects
  Let PC handle user interaction, while microcontrollers like AVR/ATmega manage the hardware

## Slide 16: Language Choices
Visual BASIC
  Less intimidating for the novice programmer
  Lots of UI toolkits and third-party libraries
  No cross-platform capabilities -- Windows PC only!
  Low performance -- not easy to take advantage of PC hardware capabilities

## Slide 17: Language Choices
C/C++
  Enough rope to shoot yourself in the foot
  But: can be very easy to read and write with a little self-control!
  Very high performance
  Very general -- everything from UI code to DSP
  Inherently platform-independent
  Many systems-level programmers already know it
  Plenty of free compilers
    Microsoft Visual C++ command-line compiler for Win32
    OpenWatcom for Win32 or DOS
    GCC for Win32, DOS, Linux, Atmel... everything

## Slide 18: Language Choices
C#
  Cross-platform for Windows, Linux (via Mono), but no embedded support yet
  Still unfamiliar to many people
  Not a strong candidate for device programming at this time
Java
  Originally intended for device programming
  May be a good solution depending on platform support

## Slide 19: Talking to the Chips
Both DDS and PLL chips are 3-wire serial programmable
Many other parts work this way, too (volume controls, RF/IF subsystems…)
  Data
    Command and data bits shifted in 1 bit at a time
  Clock
    Shifts control/data bits into input register
    ADF411x PLLs use 24-bit words
    LMX23x6 PLLs use 21-bit words
    AD9852/4 DDS uses 8-bit words
  Latch
    Tells chip to copy input register to specified command register
    Command register selection is typically part of the input word itself
    LMX23x6 PLL data sheet calls this LE (“Load Enable”)
    ADF411x PLL calls this LE (“Latch Enable”)
    AD9852/4 DDS calls it I/O UD CLK
    Same function in all cases! Software toggles the Latch line after all Data bits for a given command have been Clocked in

## Slide 20: Talking to the Chips
Above timing diagram from National Semiconductor LMX23x6 data sheet, but (again) applies to all parts being discussed
AD9852/4 DDS also has two Reset lines
  MASTER RESET clears entire chip state
    Intended to be asserted at power-up
  I/O RESET clears I/O interface state only
    Not needed in most designs

## Slide 21: PLL Software Design Example
KE5FX/VK6BRO hybrid synthesizer described in Mar/Apr 2004 QEX
Reproducible project, no R&D needed
Off-the-shelf parts used throughout
< 1 GHz - 7 GHz range depending on component choice
Tunable in 1 Hz steps
Cross-platform C++ control software compatible with both Win32 and Atmel

## Slide 22: The Synthesizer Control API
Public interface to synthesizer supports three basic operations
  Construction of SYNTH class instance
    Application must create one SYNTH instance per synthesizer to be controlled, specifying its parameters
      PLL chip type
      Minimum output frequency
      DDS center and reference-clock frequencies
      DDS clock multiplier range
  Frequency control
    SYNTH::set_frequency(U64 hertz)
    64-bit parameter specifies frequencies to 1.8E+19 Hz with 1 Hz precision
  Status polling
    BOOL SYNTH::locked()
    Determines time-to-lock in test programs
    Helps detect hardware failures

## Slide 23: SYNTH Construction
Derive programming constants needed later
  Precalculate as much as possible to save CPU time when setting the frequency
Initialize the PLL chip
Initialize the DDS chip

## Slide 24: Derive Programming Constants
Pick a reference modulus (R divisor)
  Determines nominal PLL comparison frequency (Fcomp)
  Higher Fcomps usually lead to lower phase noise, up to a point
  14-bit precision
    1-16383 for ADF411x
    3-16383 for LMX23x6
  We choose R=11 to yield Fcomp = ~1 MHz for 10.7 MHz DDS output
Calculate DDS tuning range
  DDS_BW = (DDS center frequency2) / (min_output_freq * R)
  About 10.4 kHz for 1-2 GHz output with 10.7 MHz DDS and R=11
  Max/min Fcomp = 10.7 MHz +/- (DDS_BW / 2)
  Post-DDS filter passband needs to be this wide

## Slide 25: Derive Programming Constants
Pick a prescaler modulus (P divisor)
  LMX2306 (550 MHz) chips are hardwired to P=8/9
  LMX2316 / 26 (1.2 / 2.8 GHz) chips are hardwired to P=32/33
  ADF411x chips allow selection of P=8/9, 16/17, 32/33, or 64/65
  Maximum prescaler output frequency is limited by spec
    < 200 MHz for ADF4112 at Vcc=5V
    Determined by chip’s max frequency for National LMX parts
  For ADF411x parts, we select largest P that satisfies minimum-N relation for dual-modulus prescalers
    min_N = min_output_freq / max_Fcomp
    P*P - P must always be <= min_N
    Example: min_N = 1027 at 1 GHz, so we choose P=32/33 (P*P - P = 992)

## Slide 26: Initialize the PLL Chip
Analog Devices ADF411x
  Send 24-bit LATCH_INIT control word
    Enable digital lock detection
    Select charge-pump gain Kpfd
      We use Kpfd = 1.88 mA
      Higher values up to 5 mA are possible and may improve PN in some loops
    Select prescaler divisor P, chosen earlier
  Send 24-bit LATCH_R control word
    Set 14-bit R modulus (typically 11)
    Set lock-detect precision = high
National Semiconductor LMX23x6
  Send 21-bit LATCH_INIT control word
    Enable digital lock detection
  Send 21-bit LATCH_R control word
    Set 14-bit R modulus (typically 11)
    Set lock-detect precision = high

## Slide 27: Initialize the AD9852/4 DDS
Assert MASTER RESET for at least 10 reference clock cycles
  This initializes the DDS chip, leaving it in “auto-update” mode by default
  Auto-update = very annoying feature that we want to turn off ASAP
Write four 8-bit words to DDS control register 7 to configure chip
  Disable internal comparator, quadrature DAC, and inverse-sinc filter
  Default to minimum clock-multiplication factor
  Set single-tone output mode
  Disable auto-update mode
  Enable AM amplitude-scaling register for improved spur performance
Wait for one auto-update period (~1 uS at 100 MHz)
  This ensures that the command to disable auto-updates has been processed by the chip. But...
  The last part of the register write may have been interrupted by the final auto-update cycle! So...
We must repeat the control-register write operation, this time followed by a manually-issued I/O UD CLK (“Latch”) toggle

## Slide 28: SYNTH Frequency Control
SYNTH::set_frequency(U64 hertz)
  Calculate optimal DDS clock multiplier
  Calculate required PLL N divisor
  Calculate required DDS output frequency
  Program DDS output frequency and CM
  Program PLL’s N divisor register
  Return to application, which may begin polling for loop lockup…
Perform calculations up front to minimize time spent in unlocked/invalid state

## Slide 29: SYNTH Frequency Control
Calculate optimal DDS clock multiplier CM for specified output frequency
  DDS_CLK = product of CM and DDS clock input
  Our DDS_CLK range = 80-120 MHz
    CM = 8-12 for 10 MHz input
  We want to maximize abs(output frequency in Hz - closest harmonic of either DDS_CLK/2 or DDS_CLK/3) to avoid output spurs due to intermod effects
  Code uses brute-force nested search loops, could probably be optimized further
  This wouldn’t be necessary if the DDS were in its own shielded/decoupled enclosure away from the rest of the PLL

## Slide 30: SYNTH Frequency Control
Calculate required PLL N divisor
  N = output frequency Hz / minimum Fcomp, rounded down to integer
  C/C++ typecast to int does this automatically
Calculate required DDS output frequency D
  Actual comparison frequency (Fcomp) = output Hz / N
  Multiply Fcomp by R to obtain required DDS output frequency D
    D = R * (Hz / N), but…
    Don’t divide by N just yet! Start with the numerator (Hz)…
    Multiply by R divisor
    Shift left 8 bits to yield 56:8 fixed-point value
    Perform /N after the multiplication above to avoid losing LSBs
    Actual expression: D = ((Hz * S64(R)) << 8) / N
    Remember: division costs precision that multiplication/shifts can’t restore. Multiply first, then divide.

## Slide 31: SYNTH Frequency Control
Program DDS clock multiplier CM
  Setting new CM requires full DDS initialization, so make sure it’s actually changed!
Program required DDS output frequency D
  Desired 48-bit DDS phase-increment register value = (D << 48) / DDS_CLK
  Again, we use fixed-point math techniques to maintain precision where it’s needed
    Incoming D is in 56:8 format
      Note that if D = ~10.7 MHz, the actual D value occupies about 24:8 bits
    Shift D left by 28 bits, leaving it in 28:36 format
    Divide by DDS_CLK
      This is equivalent to shifting right by log2(DDS_CLK) bits (about 26.5 bits if DDS_CLK = 100 MHz)
      Because 28 > 26.5, we still have all the precision we started with!
    Shift left by 12 bits to convert to 0:48 DDS phase-increment register format
    Send lower 48 bits to DDS chip’s phase-increment register
      Transmitted as 6 8-bit words before toggling LATCH

## Slide 32: SYNTH Frequency Control
Program PLL’s N divisor
  We already had to calculate N to determine DDS output frequency
  Check to make sure N has actually changed, to avoid breaking phase continuity
    Remember, small changes in frequency are the DDS’s job
  Send 21- or 24-bit LATCH_N command with N data
    PLL chips break N into two sub-registers, A and B
      B = N / P
      A = N - (B * P)
    ADF411x N-register = 19-bit word BBBBBBBBBBBBBAAAAAA
    LMX23x6 N-register = 18-bit word BBBBBBBBBBBBBAAAAA
    LMX23x6: Also set bit 20 for high Kpfd (1 mA at Vcc=3V)
    Good idea to sanity-check the A/B values against the chip specs
  At this point, PLL and DDS chips are fully programmed. Loop will now commence locking.

## Slide 33: Lock-Detection Status Polling
BOOL SYNTH::locked()
  Return TRUE when PLL lock detection signal goes TRUE
  Simply reads the input port associated with the PLL chip’s LD pin (Lock Detect)
    LD = the only output pin read by the host
  PLL chip has previously been programmed for high-precision lock detection
    Goes TRUE when phase error is < 15 ns for 5 consecutive cycles of Fcomp
    Remains TRUE until phase error of > 25 ns is detected on any subsequent cycle

## Slide 34: Lockup Performance
Purple/blue: KE5FX hybrid synthesizer, 1000-2000 MHz and back
Green/red: ICOM IC-R7000 1st LO, 770-1030 MHz and back

## Slide 35: Noise Performance
Purple: KE5FX hybrid synthesizer, -83.7 dBc/Hz at 1 kHz from carrier
Blue: ICOM IC-R7000 1st LO, -70.5 dBc/Hz at 1 kHz from carrier

## Slide 36: PC Client Application
Win9x, Win2K, WinXP console application for synthesizer testing
Also runs under MS-DOS when built with OpenWatcom compiler
Supports Tektronix 49x / HP 8566 analyzer control for automated tests via GPIB

## Slide 37: Atmel Control Terminal
Hosted via RS-232 port on ATmega128
Same capabilities, same API, same code as Win32 app
  Win32 console application was built with Microsoft Visual C++
  Atmel terminal application was built with AVR-GCC

## Slide 38: Typical Embedded Application
Fully self-contained 800 MHz data radio
  Single-conversion FM receiver based on Atmel ATmega128 microcontroller, KE5FX hybrid synth, and Philips SA604AD IF subsystem
  16 MHz ATmega128 is fast enough to decode Motorola Type II SmartNet trunk control channel (3600 bps FSK) in real time
    Software demodulator written in 32-bit C++
    Almost a straight port of motorola.cpp from well-known “Trunker” application
    Sends decoded traffic to PC via RS-232 at 38400 bps
  Needs only power, antenna, 10 MHz PLL reference, and RS-232 connections
  Fits in a single Hammond 1590BB enclosure (4.6” x 3.6” x 1.3”)

## Slide 39: Experimental Hybrid YIG PLL
2-6 GHz tuning range
Better than -100 dBc/Hz PN at 10 kHz
  HP 8672A-class performance
Simple modifications to synth platform
  ADF4107 PLL IC (7 GHz max freq)
  Emitter follower instead of VCO
    Drives YIG FM tuning coil
  YIG pretuned by MAX541 16-bit serial DAC
    Driven by second PC parallel port

## Slide 40: Conclusion: Design Resources
Full schematics and software for KE5FX/VK6BRO hybrid synth
  www.qsl.net/ke5fx/synth.html
John Miles, KE5FX, and Richard Hosking, VK6BRO, “A Versatile Hybrid Synthesizer,” QEX, Mar-Apr 2004
    Also available online at www.qsl.net/ke5fx/synth.html
National Semiconductor WEBENCH design tool (http://wireless.national.com)
Analog Devices ADIsimPLL design tool (www.analog.com)
AVR-GCC multiplatform C++ compiler (www.avrfreaks.net/AVRGCC/)
PLL Performance, Simulation, and Design by Dean Banerjee (available at Amazon or at WEBENCH site above)
KE5FX Projects group for ongoing discussion (http://groups.yahoo.com/group/ke5fx/)