## Slide 1: Introduction to HSMM for the microwave astute
W5HN
North
Texas
Microwave
Society
NTMS
John Beadles – N5OOM
North Texas Microwave Society

## Slide 2: The goal of this presentation
The goal of this presentation is to provide operators who are more used to the technical side of microwave operation with an overview of what is going on in the data side of the technology, what is needed, and what you can help with.
This is not a particularly technical presentation. There isn’t a single graph in the whole darn thing. Sorry!

## Slide 3: What the heck is HSMM?
HSMM, or High Speed Multimedia, is the name of an ARRL sponsored technical project to introduce high speed data radio (56 kbps & higher) to amateur radio.
HSMM generally provides a link for standard internet protocols. Regular applications such as web, ftp, email and other applications can run over it without modification.
The popular license free 802.11a/b/g services operate on bands that overlap amateur frequency allocations, giving us cheap hardware that can be used in in part 97 operation… but with complications.
HSMM is intended more for operational networks rather than contesting, though distance contests are common. Persons interested more in experimentation will have plenty of room for fun.

## Slide 4: ARRL HSMM Working Group
HSMM development is being sponsored by the ARRL HSMM Working Group
Instituted in January 2001 by ARRL BoD
  Dr. John Champa, K8OCL, Chairman
Several sub-projects
  HSMM-HF Project (ODFM on 25KHz of spectrum, 70kbps)
  Bi-Directional Amplifier Project
  ODFM Modem project
  Misc member projects
For more information:
  Website: http://www.arrl.org/hsmm/
  eMail List: http://listserv.tamu.edu/archives/arrl-80211b.html

## Slide 5: The HSMM WG focus:
ARRL Guidance
  Frequency allocations
  Modulation regulations
  Power limits
  Band Plans
  Encryption / Security
Technology Development
  High data rate modulations in various frequency bands
  Network Security
Operating Practice
  Identification
  IP assignment (v4 and v6)
  Installation
  Network design
  Network protection
Hardware
  Radios
  Antennas
  Power Amplifiers
  Transverters
  Power over Ethernet

## Slide 6: Local Organizations
Michigan
  Livingston County Hinternet Org
  Oakland County HSMM Org
Texas
  North Texas Microwave Society – HSMM WG (D/FW)
  San Antonio, TX ARRL 802.11 org
Others

## Slide 7: How does HSMM work
HSMM is generally intended to connect computer networks
  But not always…
Uses packet techniques
  Standard TCP/IP is prevalent
Can use larger than normal bandwidths
  up to 25 MHz
Uses various modulation schemes
  ODFM
  BPSK
  QPSK
  Etc…
Equipment can often dynamically switch modulations to get the lowest bit error rate rate for current conditions
To get the wide bandwidths necessary, HSMM equipment often operates in the UHF and above bands.
QRP operation is typical, with xmit powers from 20mw and higher

## Slide 8: Relevant FCC Rules
97.301 Authorized frequency bands
97.305 Authorized emission types
  SS, data on all bands 70cm and higher
97.331 SS emission types
  100W max tx pwr
  Must use automatic power control if over 1W

## Slide 9: FCC Rules Changes
FCC NPRM 04-79
  Notes that previous rules were adopted in 1985, no negative effects noted since that time
  would permit spread spectrum operations in 1.25m band
  Request for comments for permitting SS operation in 2m, 6m bands

## Slide 10: HSMM Applications
Hospital / EOC interconnects
Document Storage & Access
Document and Printer Sharing
IRLP Repeater Links
APRS Internet Feed
Local Public Service Event Management
Internet-based Weather Services
Regular Internet Service
Web based applications

## Slide 11: Radio Metropolitan Area Network (RMAN)
900MHz
5.8 GHz
2.4 GHz
D-star
1.2 GHz
Emcomm
Access Point
Satellite Uplink

## Slide 12: Emergency Deployment Access Point
Net Controls
Served Agency Liasons
Weather Liasons
Health & Welfare Liasons
Access Point for
Local Distribution
Bridge to an internet connection
DSL Router
Computer configured as an EMCOMM Server
Equipment in weatherproof boxes
Power run up the Ethernet cable

## Slide 13: Ham Equipment
Generally available ham equipment is limited
Icom D-STAR
  Runs on 1.2 GHZ, combines FM voice and 128kb data
  Requires separate, proprietary analog and digital repeaters
  System of components including mobile radio, voice and data repeaters and a 10GHz backhaul radio
  Mobile has ethernet, USB connections
  Pricey!
  http://www.icomamerica.com/amateur/dstar/
Icom IC-2200
  2m mobile radio
  Optional modules provides 4.8kb data
  Data connection type unknown – serial port?
  Price in the $200+ range not including digital option
Custom stuff?

## Slide 14: Consumer Equipment
Some consumer / commercial equipment can be pressed into service as ham HSMM gear, particularly 802.11x gear
802.11 is an IEEE standard for wireless data networking
  802.11 runs in 2.4 GHz provides up to 2mbps
  802.11b runs in 2.4 GHz, provides up to 11mbps
  802.11g runs in 2.4 GHz, provides up to 54mbps
  802.11a runs in 5 GHz, provides up to 54mbps
  The speed difference is based on modulation
Consumer 802.11 equipment runs under FCC part 15 rules for “license free” operation
  But the part 15 freq allocations overlap ham allocations
Most newer 801.11x radios are backward compatible (within the same frequency band)
Proprietary connectors (Reverse Polarity N, TNC, SMA, MC, MMCX) per FCC requirement

## Slide 15
2.4 GHz (802.11b/g)
802.11b channels 1-6 overlap amateur allocations
AMSAT requests not to use ch 1 due to sat interference
11 overlapping 802.11b/g channels
11 MHz wide each, 5 MHz spacing

## Slide 16
5 GHz (802.11a)
12 non-overlapping 802.11a channels
20 MHz wide each
3 sets of 4 channels
  4x40mw ch for indoor
  4x200mw ch for indoor, outdoor
  4x800mw ch for outdoor
  Power specified at the IR
More bandwidth requested

## Slide 17: So what needs doing?
Policy
  General participation!
Hardware
  Data modem / radios
  Bi-directional power amplifiers
  Transverters
  Cheap test equipment suitable to the modulations in use
  Field useable packaging
  Antennas
Software
  Network monitoring tools
  Network security tools
  Ham specific messaging applications

## Slide 18: Network Planning with Radio Mobile
Needs: Need a user doc describing how to use RM for HSMM design. Also need a library of antenna patterns and equipment power / receive sensitivity
Also need a good way to incorporate terrain obstacles

## Slide 19: Wireless Connections for the ’04 Wild Ride

## Slide 20: Network plan for the ’04 Wild Ride

## Slide 21: Path Testing for the ’04 Wild Ride
KD5YVL at Lavonia Park
20mw works at 13.6 miles!!!
KD5OUG, N5OOM and KD8VL

## Slide 22: Bridge Installation at the Lake Lavon Army Corps of Engineers tower
Packaged
Linksys
WAP11
KD5MNO
N5OOM
KD5MNO
KD5YVL
KD5PQA

## Slide 23: Information Resources
ARRL HSMM Group
  The group that started this mess
  http://www.arrl.org/hsmm/
  http://listserv.tamu.edu/archives/arrl-80211b.html
NTMS HSMM email list
  http://groups.yahoo.com/group/ntms-hsmm/
HAMCOM HSMM Presentations
  http://www.n5oom.org/2004_hamcom/presentations.htm
Seattle Wireless
  Large equipment reference list
  http://www.seattlewireless.net/\
O’Reilly Books
  Standard books on 802.11x networking, security
  http://www.oreilly.com/
eBay
  Lots of cheap networking gear and antennas (search on WiFi)
  http://www.ebay.com
Fleeman, Anderson and Bird
  Ham 802.11x suppliers (state “HSMM” for discount!)
  http://www.fab-corp.com/

## Slide 24: Useful O’Reilly Books
And coming soon to the the ARRL Library:
These two books will get you up to speed on wireless networking
(available from the ARRL catalog or your local bookstore)