## Slide 1: Tropospheric enhancement VHF and up What causes band openings? How can you find them?
W5HN
North
Texas
Microwave
Society
NTMS
Joe Jurecka-N5PYK
North Texas Microwave Society

## Slide 2: What is an opening?
Characterized by radio propagation enabling communications at distances significantly beyond line-of-sight.
Typically affects 50 MHz and up
Caused by changes in air refractivity with height
Similar to light in a fiber optic

## Slide 3: Types of Openings
TropoScatter
  Available most all the time. Contacts made with brute force (so to speak).
Local Enhancement
  Enhances signals that would otherwise be weak
  Nominally a single hop off an inversion layer
Tropospheric Ducting
  Regional
    Openings within an area such as Texas
  Wide Area
    Texas to Florida or Yucatan
    Texas to Illinois or Virginia

## Slide 4: Troposcatter (Not ducting—but still useful and reliable)
http://www.qsl.net/oz1rh/troposcatter99/troposcatter99.htm
This mode of propagation is what is primarily used in those awful dead-band conditions during contest weekends. An abundance of power is how this mode pushes through where as ducting, in the best conditions, allows good propagation with “low” ERP!
This mode is why N5PYK can work W3XO near Kerrville or K5TR in Johnson City any time day or night from EM13qe.
Gain antennas plus a little power = DX

## Slide 5: Troposcatter and Emrg. Comms
Reliable regional communications with modest antenna setup
Atmospheric noise (lightning) less influential
15-20’ high antenna helps tremendously
25-50W all that is required
Antennas may often be attic mounted!
Reliable paths include DFW to Austin, Shreveport, Lawton, Abilene, Bryan, etc.
A little more antenna gain or power enables Houston, San Antonio, Oklahoma City, Tulsa and beyond

## Slide 6: Sounding Stations
Launch balloons twice a day:
00Z and 12Z
During spring, an 18Z sounding is not uncommon in thunderstorm risk areas

## Slide 7: Local Enhancement (Tropospheric Refraction)
Present most evenings in eastern Texas
Accomplished with single hop off inversion layer aloft
Often a single inversion layer aloft…sometimes very close to the ground
Very useful on microwave on spring and summer evenings!
10GHz 2001 Contest
Boyd to WA5JAT-- 10GHz signals peaked at 6 degrees above horizon. Corresponded exactly with location of inversion aloft that evening
http://electronics.howstuffworks.com/fiber-optic6.htm

## Slide 8: K=Factor
Openings are large areas of consistent, favorable conditions
Ratio of effective radius of radio wave ray vs. radius of earth (6370km)
Optical line of sight
Radio horizon
Normally about a 1.4X distance multiplier on VHF.
Important for understanding local enhancement
K=r/r0

## Slide 9: Schematic of Profile (Refraction)
Openings are large areas of consistent, favorable conditions
N=77.6/T[P+(4810*Es*(RH))/T) ‡FREEMAN
N=Refractivity
Es=Saturation Water vapor pressure (mB)
RH=Relative Humidity
T=Temperature (Kelvin)
P=Atmospheric pressure (mB)
N is refractivity…similar to n in fiber optics
Ingredients Temperature, Moisture, and Pressure
Larger N = slower propagation
K≈[1+(∆N/∆h)/157]^-1
K=K-factor
N=Refractivity
h=height (km)
N≈(n-1)*10^6 where n=ratio of speed of propagation to speed of light
Es=(1.0003+P*0.00000418)*6.1115*EXP(22.425*DP/(272.55+DP)) If DP >0 C
Es=(1.0007+P*0.00000346)*6.1121*EXP(17.502*DP/(240.9+DP)) If DP <0 C
DP=Dewpoint (Deg C) *Source Honeywell Website
Higher Index (Slower propagation) N=350
Lower (Faster propagation) N=243
LOS
Radio waves are “bent” toward area of higher index of refraction (higher N, lower velocity)

## Slide 10: Upper Air sounding (refraction)
Taken from
Opening in
Early May 98
Temperature
Dewpoint
Height in millibars
10 Deg
inversion
@925mB N=243
@975mB N=351
Example of a surface duct right on the deck

## Slide 11: Tropo Ducting
Can enable contacts over distances of over a thousand miles.
RF signal is propagated in duct
Much variance exists on where signal exits the duct
Signal can pass right over some users such that it is possible to work stations in Florida but not Mississippi

## Slide 12: Schematic of Profile (Duct)
Openings are large areas of consistent, favorable conditions
N=77.6/T[P+(4810*Es*(RH))/T) ‡FREEMAN
N=Refractivity
Es=Saturation Water vapor pressure (mB)
RH=Relative Humidity
T=Temperature (Kelvin)
P=Atmospheric pressure (mB)
N is refractivity…similar to n in fiber optics
Ingredients Temperature, Moisture, and Pressure
Larger N = slower propagation
K≈[1+(∆N/∆h)/157]^-1
K=K-factor
N=Refractivity
h=height (km)
N≈(n-1)*10^6 where n=ratio of speed of propagation to speed of light
Es=(1.0003+P*0.00000418)*6.1115*EXP(22.425*DP/(272.55+DP)) If DP >0 C
Es=(1.0007+P*0.00000346)*6.1121*EXP(17.502*DP/(240.9+DP)) If DP <0 C
DP=Dewpoint (Deg C) *Source Honeywell Website
Higher Index (Slower propagation) N=350
Lower (Faster propagation) N=243
Lower (Faster propagation) N=330
LOS

## Slide 13: Upper Air Sounding (Ducting)
This opening
Provided an opening
Strong enough to
Hear NOAA weather
Radio out of Hobbs
New Mexico using
A 5/8λ whip antenna…
Traveling
US-75 in Allen
Soundings are taken at 00Z and 12Z
Dewpoint
Temperature
6.5 degree
Temperature inversion
Two inversions form a duct
DUCT

## Slide 14: Duct thickness vs frequency
From http://www.iprimus.ca/~hepburnw/dx/luf.htm

## Slide 15: Unfavorable sounding
Here, we have an inversion, but…No opening.
Note lack of dewpoint drop at base of inversion layer.
May provide local enhancements to upper bands, but may not be enough for 144MHz.
This profile is typical for cold air intruding at sfc with warm, overrunning conditions aloft. Good for rain…not for propagation.
Note: North winds down low

## Slide 16: The Feb 2, 2003 Opening
Produced opening
From Texas to Florida
On 144 - 3456 MHz
Note absence of significant weather features along path.
No pressure discontinuities (fronts)
Providing indication of a stable weather pattern. Front approaching from NW is typical for evening for opening.

## Slide 17: Mount Scott to Dallas on 10GHz
Propagation in the morning was very difficult, but signals came up throughout the day. Notice how the profile becomes more “classic” from 12Z to 18Z to 0Z

## Slide 18: Surface Pattern

## Slide 19: Monitoring for Openings
TV - Local channels will get interference patterns or a separate set of sync bars
Listen for UHF TV video carriers (Ch16-KLRT Little Rock, AR 483.25)
Using TV is becoming more difficult with so many digital stations starting service on what used to be clear channels

## Slide 20: Monitoring for Openings
VHF Aircraft Navigation Aids (VOR-very high frequency omnidirectional range)
108-117.95 MHz.
www.airnav.com
50-200W ERP Horizontal Pol.
Listen for 30Hz sidebands if listening on USB/LSB (Sounds like a warbling carrier). Tune up / down 1KHz to hear carrier
Significant co-channel spacing

## Slide 21: Weather Radar Signatures
http://www.srh.noaa.gov/radar/mosaic/DS.p19r0/ar.us.conus.shtml
Look for ground clutter extending out 50-100 miles from a site (>+10dBz).
Look at individual sites and note mode of operation
  Clear Air- most sensitive…will often detect clouds (Scale up to +28dBz)
  Precipitation Mode: More traditional scaling that users are used to seeing Scale (up to 70dBz)
  National mosaic is de-cluttered precipitation mode view.
dBz scale
  <0 normally clouds, mist or light snow
  0-40 rain
  40-60 Thunderstorm
  >60 Potential severe thunderstorm
  >70 Nasty hail core
If it looks like this in clear air mode, you might as well work on a project.
dBz scale
Nexrad (WSR-88D) operates around 3 GHz
Enhancement in precip mode
Enhancement in Clear air mode

## Slide 22: Radar View
Inversion layer showing
up on Range-Height
depiction on radar
*Battan

## Slide 23: Hepburn Tropo Index
http://www.iprimus.ca/~hepburnw/tropo_car.html
Good general indicator of forecasted conditions.
Not definitive indicator of when and where an opening will occur—This is not an exact science.
Usually, when there is a lot of yellow, orange, and red, it is wise to at least check conditions more carefully.

## Slide 24: Other sources
NOAA Weather radio 162.4-162.55 http://www.srh.noaa.gov/ftproot/msd/nwr/srnwr.html
http://dxworld.com/144prop.html
Monitor 144.200
Propagation Beacons
  http://www.ntms.org/Beacons.htm
  http://www.k5rmg.org/beacons.html
http://www.rap.ucar.edu/weather/upper/
http://weather.unisys.com/upper_air/skew/index.html
Texas DPS 155.46, 159.210, 155.445

## Slide 25: References
Freeman, R.L. Radio System Design for Telecommunications (1-100 GHz) John Wiley,1987. ,
Battan, Louis J., Radar Observation of the Atmosphere, University of Chicago Press, Chicago, IL., 1973.
Other good reading
Preben-Hansen (OZ1RH), “Everyday VHF, UHF, and SHF propagation – 700 km DX anytime using troposcatter” http://www.qsl.net/oz1rh/troposcatter99/troposcatter99.htm
Microwave activity www.ntms.org