## Slide 1: CURRENT AND FUTURE MICROWAVE SATELLITES
CURRENT and FUTURE MICROWAVE SATELLITES
October 2004 Status Report
Presented by
Keith Pugh, W5IU
Microwave Update Conference
Dallas/Fort Worth, TX,
Saturday October 16 2004

## Slide 2: CURRENT AND FUTURE MICROWAVE SATELLITES
CURRENT MICROWAVE SATELLITES
  AO-51 – “Echo”
  UO-11
FUTURE MICROWAVE SATELLITES
  SSETI Express – AMSAT-UK
  PHASE 3-E (Express) – AMSAT-DL
  EAGLE – AMSAT-NA
AMSAT’s VISION
“Our Vision is to deploy high earth orbit satellite systems that offer daily coverage by 2009 and continuous coverage by 2012…”

## Slide 3: AMSAT OSCAR-E (“Echo”) now AO-51
AMSAT AO-E Project
July 2004 Status Report
Presented by
Robin Haighton VE3FRH
for
Richard M. Hambly, W2GPS
19th AMSAT-UK Colloquium at the
University of Surrey,
Saturday July 31 2004

## Slide 4: AO-E Technical Overview

## Slide 5: AMSAT OSCAR-E (“Echo”) Communications Block Diagram
2 Modulators
Multi-Band Multi-Mode Rx
VHF Rx
UHF Tx
6 Demodulators
Switching Matrix

## Slide 6: AMSAT OSCAR-E (“Echo”) Integration
Integration began December 8, 2003
  Jim White WD0E and Mike Kingery KE4AZN arrived at SpaceQuest in Fairfax VA.
Details in Jan/Feb AMSAT Journal.
Project Manager Dick Daniels W4PUJ watching over Integration Team Leader Jim White WD0E at SpaceQuest on 18-Dec-03.

## Slide 7: AO-E RF Subsystems Receivers
4 miniature VHF FM receivers
  <40 mW each
  <40 gm each
Each receiver has 2-channel capability
Sensitivity is -121dbm for 12db SINAD
VHF PreAmp/Filters
Interface Board
Four VHF Receivers
4-Way Power Splitter

## Slide 8: AO-E RF Subsystems Transmitters
Two UHF FM transmitters that can be operated simultaneously.
1-6 watts out.
Frequency agile in 2.5KHz steps, tunable over about 20 MHz.
UHF Hybrid Combiner
Transmitters

## Slide 9: AO-E RF Subsystems Multi-band Receiver
All-mode, 10m, 2m, 70cm and 23cm.
Performance limited by broadband antenna.
Multi Mode Receiver
is under the
UHF Hybrid Combiner

## Slide 10: AO-E RF Subsystems 2.4 GHz S-Band Transmitter
Exciter & interface board.
  Chuck Schultz KE4NNF
Exciter draws 38.3 mA
+5.0 dBm output.

## Slide 11: AMSAT OSCAR-E (“Echo”) Mode L/S Hardware Update
Chuck Schultz KE4NNF designed the exciter and Charlie Suckling G3WDG designed the power amplifier. Lou McFadin W5DID mounted wired the modules. Photo by Stan Wood WA4NFY.
Dual band antenna 1268.700 MHz up 2401.200 MHz down designed by Stan Wood WA4NFY.

## Slide 12: AO-E Integrated Flight Computer (IFC)
Flight proven, low-power < 300 mW,
6 Rx and 6 Tx SCC (data) channels
1 MB EDAC, 16 MB RAM,16MB flash
6 demodulators
2 modulators

## Slide 13: AO-E Spacecraft Flight Software
Spacecraft Operating System (SCOS)
  Thanks to Harold Price NK6K.
Boot Loader
  Bob Diersing N5AHD
Command And Telemetry Program
  Ground station Windows based
Boot Loader Prototype
  Ground station Windows based
Jim White WD0E’s Integration Lab
Housekeeping task

## Slide 14: AO-E Power Generation
Six high efficiency Solar Panels
  Triple junction MCORE GaAs cells (~27%).
  ~20W when not in eclipse (12-14W per side).
Mark Kanawati N4TPY carrying $20,000 worth of solar cells and sooo casually spreading glue all over

## Slide 15: AO-E Power Distribution Battery Control Regulator (BCR)
Autonomous, fail-safe.
50KHz 89% efficiency.
Keeps the spacecraft alive at all costs.
Charges the battery using only solar power, so will charge a dead battery.
Prevents the battery from overcharging or depleting.
Provides the necessary voltages and telemetry.

## Slide 16: AO-E Power Distribution Batteries
Matched set of six NiCd cells
4.4 Ah each, nominal 8 VDC.

## Slide 17: AO-E Attitude Control (Experimental)
Active magnetic attitude control.
Semi-permanent magnetic rods
Strength and polarity can be adjusted
It's possible to turn the satellite upside down.

## Slide 18: AMSAT OSCAR-E (“Echo”) Operations

## Slide 19: AMSAT OSCAR-E (“Echo”) Operations
FM voice repeater mode
  Active all the time.
  145.920 MHz uplink with 67 Hz PL tone.
  435.300 MHz downlink.
  TX comes on only when it hears a 67 Hz PL for one second and stays on for up to ten seconds after the tone disappears.
  TX power is 1 Watt may be as high as 6 Watts.

## Slide 20: AMSAT OSCAR-E (“Echo”) Operations
Digital mode
  Active all the time.
  145.860 up, 435.150 down at 9,600 baud.
  TX will be set to one Watt.
  Store and forward bulletin board system (BBS) using PACSAT Protocol Suite.
  Digital downlink will also contain telemetry.
  Whole orbit data will be available for download.
  May broadcast periodic APRS status messages.

## Slide 21: AMSAT OSCAR-E (“Echo”) Operations
Experimenters' day
  Wednesdays (UTC).
  Any other mode may be in use.
  Scheduled a week or more in advance.
  Default is digital; 1268.700 up at 9,600 baud and 2401.200 MHz down at 38,400 baud.
  Other common modes include L/S FM voice and L/S Data with 9,600 baud up and 38,400 or 76,800 baud down.

## Slide 22: AO-E Status Update Launch
Dnepr LV (SS-18) launch from Baikonur Cosmodrome in Kazakhstan, Dec 2002
Launch took place June 28, 2004
Two AprizeStar satellites by SpaceQuest ready for launch. These are very similar to AO-E.

## Slide 23: Integration of MicroSats to Space Head

## Slide 24: Space Head Loading into Silo

## Slide 25: Dnepr Launch from Silo

## Slide 26: AMSAT OSCAR-E (“Echo”) Volunteers
Mike Kingery KE4AZN for on-site support of integration testing, including the loan of his satellite station, and for developing command and telemetry ground station software.
The SpaceQuest team, especially Mark Kanawati N4TPY and Dr. Dino Lorenzini KC4YMG who are also AMSAT members and volunteers.
Jim White WD0E for his technical contributions, leadership skills and for the many hundreds of hours he has invested.
Harold Price NK6K, for his donation of the Spacecraft Operating System (SCOS) kernel and file system and for his on-site integration support.
Bob Diersing N5AHD, for his timely work on the boot loader.
Skip Hansen WB6YMH, for his efforts on the ground station software.
Chuck Schultz KE4NNF, Charlie Suckling G3WDG, Lou McFadin W5DID and Stan Wood WA4NFY for their work on the S-band transmitter and L/S band antenna system.
The AMSAT project management team for their help and assistance,
Tom Clark W3IWI, Rick Hambly W2GPS and Dick Daniels W4PUJ.
David Bern W2LNX, for his assistance with the ground station hardware.
Special recognition is due to the following for their contributions and support during the integration phase of the Echo project:

## Slide 27: SSETI Express – AMSAT-UK
“Short Fuse” project in conjunction with European Space Agency (ESA) for Education Outreach
  Launch in late 2004 or early 2005 on Ariane
  Low Earth Orbit
  Original Purpose – Support Student Experiments
    U Band command uplink
    S Band data downlink
  When Experiments are complete – turn over for use as an Amateur Radio Mode U/S transponder
  Hardware Design – Common with other satellites
    S Band PA common with AO-51

## Slide 28: PHASE 3-E (Express) – AMSAT-DL
AMSAT-DL initiative to fill gap left by failure of AO-40 in Feb. 2004
  High earth orbit
  Phase 3-A/B Space Frame
  Maximum use of existing design from AO-40 and other satellites
  Launch in late 2005 or early 2006
    Probable Ariane launch – others under consideration
  Uplinks on V, U, L, & S
  Downlinks on U, S, X, & K
  Other experiments under evaluation

## Slide 29: What’s Next? (from AMSAT-NA)
0.162Cu M ~100Kg
High Eliptical Orbit
About 120 Watt power budget
Eagle!

## Slide 30: Eagle Implementation
Management Team in place
Design Team in place
Requirements defined
Maximum use of “SDR” techniques
Features “C-C Rider” concept developed by Tom Clark, W3IWI, as presented at 2003 and 2004 AMSAT-NA Symposiums
Fund Raising – Critical
“Phase 3-E” and two “Eagles” will fulfill AMSAT’s Vision

## Slide 31: Eagle Requirements
1.0 Mass, 100 Kg or less
2.0 Size 600 mm x 600 mm x 450 mm
3.0 Stabilization Spin stabilized
4.0 Orbit HEO
5.0 Attitude control
5.1 Magnetorquers and nutation dampers
5.2.Earth sensor
5.3 Sun Sensor
5.4 Stabilization to required attitude within 72 Hrs
6.0 Thermal Control
6.1 Battery Temperature -15 C to +15 C
6.2 Electronics Temperature -25 to + 40C

## Slide 32: Eagle Requirements
7.0 Power Generation
7.1 2 Fixed & 4 deployable solar panels with omni Coverage
7.2 Fault tolerant BCR and battery system that fails in operational mode.
7.3 Buss Voltage 10 to 14 Volts nominal
8.0 Propulsion
8.1` The simplest system to provide right orbit & is acceptable to launch agency – Initial estimate to provide 60 delta V
8.2 The propulsion system sho0uld be modular

## Slide 33: Eagle Requirements
9.0 Structure
9.1 Aluminum Honeycomb panels forming core structure supporting internal modules and integrated separation interface.
9.2 Separation interface is located on the –Z side, and is launcher dependent.
9.3 consider the possibility of side mounting.
10.0 Housekeeping
10.1 IHU-3 ?
10.2 CAN-Do Information Bus

## Slide 34: Eagle Requirements
11.0 Antennas.
11.1 High Gain on +Z
11.1.1 U-Band (435 MHz), L-Band (1.2 GHz),
S-Band (2.4 GHz), C-Band (5.6 GHz)
11.2 Onmi Antennas on –Z (Functional in all attitudes), V (145 MHz), U. L. & S.
11.3 Onmi Antennas +Z, U, L, S.

## Slide 35: Eagle Requirements
12.0 Payloads.
12.1 Transmitters
12.1.1 V-Band 20KHz Bandwidth – SDR Techniques
12.1.2 S-Band –two of them – Redundant.
12.1.2.1 100KHz Bandwidth
12.1.2.2 either Tx can be driven by SDR or analog
12.1.3 C-Band wide band digital including telemetry
12.1.4 All Tx to be capable of being operated together.

## Slide 36: Eagle Requirements
12.0 Payloads continued
12.2 Receivers
12.2.1 U-Band – 100 KHz bandwidth.
12.2.2 L-Band - 100 KHz bandwidth.
12.2.3 C-Band - wideband Digital
12.3 GPS – NASA
12.4 CEDEX – SSTL
12.5 Cameras – Narrow FOV on + Z axis
Wide FOV on –Z axis, cameras to survive all beta angles

## Slide 37: Eagle Requirements
        Payloads Continued
        12.6 Telemetry Beacons
        12.6.1 to be active on all transmitters.
        12.7 Command uplinks
        To be on both U and L receivers
        13.0 Magnetic environment.
        13.1 The satellite is to be as magnetically clean as possible