## Slide 1: Study of the Bands 420 MHz – 24.25 GHz
Regulatory Issues and Allocation Status

## Slide 2
The following is a brief listing of current regulatory issues affecting the UHF and Microwave Amateur Allocations. Most bands are not directly threatened, given that most are shared with Federal Government, which views the Amateur Service as a compatible sharing partner. However, recent trends toward accommodating high power unlicensed devices are a continuing threat to many microwave bands, as is the increasing commercial value of them to other radio services.

## Slide 3
United States Allocations
Amateur Service
Amateur-Satellite Service
Band (MHz)
Bandwidth (MHz)
Band (MHz)
Bandwidth (MHz)
902-928
26
-
-
1240-1300
60
1260-1270 
10
2300-2310
2390-2450
10
60
-
2400-2450
-
50
3300-3500
200
3400-3410
10
5650-5925
275
5650-5670 
5830-5850 
20
20
10000-10500
500
10450-10500
50
24000-24250
250
24000-24050
50

## Slide 4: 420-450 MHz
420-430 MHz Unavailable Above Line A.
433.92 MHz RFID Tag Systems Authorized.
449 MHz Wind Profiler Radars Moved from 406 to 449 MHz, Sites TBD.
Government Radars Primary, Amateur Secondary in Entire Band.

## Slide 5: 902-928 MHz (33 cm Band)
Orphan Band
Kitchen Sink Band
Region 2 Only
No Satellite Allocation
Little Off-the-Shelf Amateur Equipment
Little Commercial Service Competition
Upward Migration of Part 15 Devices

## Slide 6: 1240-1300 MHz (23 cm Band)
Primarily a Radar (aeronautical radionavigation) band
Numerous voice and television repeaters including crossband ATV
Weak Signal work limited to 1296 MHz
Satellite Uplink at 1260-1270 MHz
Adequate and Improving Amateur Equipment Availability
D-Star System development in this Band
Galileo commercial downlink risk at 1215-1300 MHz

## Slide 7: 2300-2305 MHz (Part of 13 cm Band)
No other U.S. Users and No Primary Service
Part of FCC Spectrum Reserve
No satellite allocation
Almost exclusive weak signal work at 2304 MHz
Possible renewal of effort by Microtrax, etc. to obtain primary allocation.
Adequate transverter and accessory availability.
Possible trade with Flight Test Telemetry for Upgrade to Primary with no Secondary User?

## Slide 8: 2305-2310 MHz (Part of 13 cm Band)
No known current amateur activity
No satellite allocation
Miscellaneous Wireless Communications Service is Primary (Auctioned) by market.
Amateur operation substantially compromised by Commercial preclusion
No current regulatory activity

## Slide 9: 2390-2395 MHz
Amateur Primary, no Secondary Allocation!
FCC Proposal in Docket 00-258 for Federal Government Relocation and Flight Test Telemetry
Compatibility/Coordination Issues

## Slide 10: 2395-2400 MHz
Amateur Primary, no Secondary Allocation!
No FCC sharing proposal.
(no amateur activity)
Some noise floor increase from Part 15 Wi-Fi and Part 18 devices in 2400-2450 MHz.
No Amateur Satellite Allocation.
Transverters available.

## Slide 11: 2400-2450 MHz
2400-2417 MHz Amateur Primary, rest Secondary
Satellite Operation Limited to 2400-2402 MHz.
Radiolocation Secondary at 2417-2450 MHz (military services only).
802.11(b) principally used.

## Slide 12: 3300-3500 MHz (9 cm band)
Radiolocation service primary; airborne search and surveillance and radars.
Candidate band for Fixed Wireless Access.
Available only in Regions 2 and 3.
Beacons and weak signal, one CA repeater.
Satellite allocation at 3400-3410 MHz.
Band Plan only for beacons at 3456.3-3456.4 MHz

## Slide 13: 5650-5725 MHz (5 cm band)
Government radiolocation primary.
5650-5670 MHz Amateur Satellite primary, all 3 regions (Uplinks only)
Available for U-NII applications (802.11)
No Amateur Terrestrial Operation

## Slide 14: 5725-5925 MHz (5 cm band)
Intelligent Transportation Systems (DSRC) from 5850-5925 MHz.
U-NII from 5725-5825 MHz.
Noise floor increase predicted at 5760 MHz due to high-power Part 15 operation.
Move to 5825-5830 MHz for weak-signal?
Minimal Government Radiolocation at 5825-5850 MHz.
Amateur-Satellite Downlink at 5830-5850 MHz

## Slide 15: 10.0-10.5 GHz (3 cm band)
Radiolocation primary (Military radars).
Heaviest used microwave band above 2450 MHz in the United States and Europe by Amateurs.
10.15-10.30 GHz band (paired with 10.5-10.65 GHz) is a candidate band for fixed wireless access.
No Amateur Satellite activity.
No domestic regulatory proposals affecting this band.

## Slide 16: 24-24.25 GHz (1.2 cm Band)
Amateur Service primary at 24.00-24.05 GHz in all 3 regions; Secondary above that.
Earth Exploration-satellite service (EESS) operates active sensors on a secondary basis.
High power Part 15 devices with directional antennas permitted above 24.05 GHz.

## Slide 17: Broader Issues
Lack of use of Microwave bands.
Ultra-wideband (UWB) between 3.1-10.6 GHz; could interfere with 3-, 5- and 10-GHz amateur bands, from nearby emitters or aggregate effects.
NTIA unwillingness to protect government allocations vs. FCC open-door policy.