## Slide 1: Millimeter-Wave LO References & Phase Noise Considerations
Presented at Microwave Update 2004
Brian Justin, WA1ZMS

## Slide 2: mm-Wave LO & Noise
Subjects covered in this talk will be:
What is phase noise?
Types of noise (ie: near & far)
Why care about phase noise?
The LO’s frequency accuracy v.s. stability
Time domain v.s. frequency domain
Frequency references (crystal, atomic, GPS)
Methods of frequency control/generation
Example of a 241GHz low noise LO and what’s possible when using one

## Slide 3: What is Phase Noise?
Phase noise is ‘random’ noise energy near an RF carrier such as a local oscillator signal. Phase noise is measured in dBc/Hz at a given frequency offset.
As the carrier frequency is increased through the LO chain, the phase noise is scaled by:
20Log(n), where n = ratio of frequencies
For example, a 10MHz signal with phase noise of -105dBc/Hz @ 1KHz would be ‘the same’ as a 1150MHz signal with -63.8dBc/Hz @ 1KHz phase noise if measured at 1150MHz.
For amateur radio purposes, phase noise can be classified as either “Near” or “Far”.

## Slide 4: What is Phase Noise?
Near phase noise affects how the signal sounds to the operator. i.e.: raspy, dirty, aurora like
Far phase noise limits the dynamic range of the receiver and also includes the broadband noise that a transmitter creates.
For this presentation, only White PM noise is considered Far noise.
All others can be considered as Near noise.

## Slide 5: Why care about Phase Noise?
Far phase noise limits dynamic range and impacts others on crowded bands.
For bands above 10GHz, near phase noise can impact DX, while far noise is less important.
Near phase noise limits narrow-band modulation techniques. i.e.: WSJT, PSK31, QRSS, etc.

## Slide 6: Frequency Accuracy & Stability
Accuracy and stability are two different metrics.
  Accuracy is a measure of precision. Think long-term. How far away from 10.0000000000… MHz are you?
  A tool used to measure accuracy is a frequency counter.
  As long as the signal is predicted to be within the IF pass-band of a receiver it’s likely accurate enough for the QSO.
  Or…..you could just tune for the signal. Once it’s found, problem solved.

## Slide 7: Frequency Accuracy & Stability
  Stability is a measure of steadiness. Think short-term. How close to 10 MHz can you maintain from moment-to-moment?
  A tool used to measure stability can be a phase noise test system. But you’ll need to do some math to convert from the frequency domain to the time domain.
  Stability determines what a signal sounds like.

## Slide 8: Frequency Accuracy & Stability

## Slide 9: Time & Frequency Domains
Not all oscillator specs are given in both time and frequency domains.
The Fourier Transform allows us to switch between the two domains.
Lucky for most of us the software has been written!
Think spectrum analyzer for frequency.
Think oscilloscope for time. But you’ll likely never see the stability error.
So measure the phase noise and count on Mr. Fourier’s help.

## Slide 10: Time & Frequency Domains
To help with measurements in the time domain the Allan Variance provides a common manifesto.
A variance is measure of how far a given value is away from the expected value.
The Allan Variance is always given for a specific time period.
For CW applications, 1-second is a good number.
An Example:
10MHz oscillator, Allan Variance 1 x 10-11 for  =1sec,
will remain within 0.0001Hz of center frequency for 1-sec

## Slide 11: Allan Variance Example
Corning MC859X4-034W 10MHz OCXO
0.1 sec 2.87 x 10-11
1.0 sec 4.38 x 10-12
10 sec 6.08 x 10-12
0.1 sec: 2.87Hz @ 100GHz
1.0 sec: 0.438Hz @ 100GHz
10 sec: 0.608Hz @ 100GHz

## Slide 12: Frequency References
Crystal Oscillator
  An old-time favorite
  Today’s best for near phase noise
  Cost… from $5 to $15k
Atomic References
  Rubidium, cheap... about $300, used
  Cesium, the cost of a nice car… about $70k, new
  H-MASER, the cost of a new house…. about $300k, new
GPS disciplined Crystal Oscillator (i.e.: HP Z-3801)
  Also cheap…..about $300, used
  Gives Cesium accuracy and OK crystal stability (maybe)

## Slide 13: Frequency References
Crystal Oscillator
  Near noise primarily depends on crystal Q
  Active device NF impacts far noise & Flicker FM
  SC-cut much better than AT-cut, better S/N
  Low frequency OCXO better than VHF OCXO even after phase noise scaling by 20Log(n)
  Don’t just heat the crystal….here’s why

## Slide 14: Frequency References
The problem is….
AT-cut crystals are designed to operate at 25degs C
If the crystal is heated it will operate on a steeper point of the temperature curve
This can make the long-term stability worse!

## Slide 15: Frequency References
Atomic Reference
  Rubidium is not the simple answer for mm-waves with narrow RX bandwidths….their choice of crystal oscillators is rather poor…..bad news for WSJT, PSK31, etc.
  Cesium and H-MASER could be used…..but costly and they too count on their internal crystal oscillators for near phase noise
GPS based
  Moderate short-term stability and near phase noise
  Limited by the choice of internal crystal oscillator as well
  But some are better than others……look

## Slide 16: Frequency References
www.leapsecond.com

## Slide 17: Frequency Reference Comparison
Allan Variance of Atomic References
Phase Noise of Various References @ 10MHz
< --- 3Hz @ 100GHz

## Slide 18: Methods of Frequency Generation
Direct multiplication
  Simple, needs filtering, 1/f noise, follows 20Log(n)
Phase locked loops
  Helpful if value of N is high
  Remember loop BW limitations
  Frequency West is good example
Direct synthesis
  Single frequency at-a-time solution, need good filtering
  Can take advantage of good near and far noise of OCXO
  Simple in concept, relies Direct Multiplication

## Slide 19: Direct Multiplier Example

## Slide 20: PLL Example/Result

## Slide 21: Direct Synthesizer Example

## Slide 22: 241GHz Example
The last ‘segmented’ RF band… 241 to 250GHz
What’s possible when you set your mind to it
Wanted VUCC #1 for the band
This example uses DM, DS, and PLL frequency generation
4 grids and several DX records, but not enough for VUCC

## Slide 23: 241GHz Example
It was all about SNR
  After Signal…..went for Noise
  10dB for every times ten bandwidth reduction
  Fighting 0.3 to 1dB/km atmospheric losses…..WX dependent
  Needed 20 more “km of signal”…..that was about 13dB
  Human ear has about 30Hz BW…..so tried Spectran
  Needed to get under 2Hz BW for desired SNR
  Knew that more signal is always helpful, therefore…..
  Aimed for 0.1Hz BW or about 4 x 10-13 for 1-second per station

## Slide 24: The Resulting LO Chain

## Slide 25: Various Oscillators

## Slide 26: Wenzel OCXO

## Slide 27: Audio Samples
47GHz with free-running 5th OT crystals
  Note the mode jumping.
75GHz with 5th OT, but frequency locked to 10MHz OCXO
  Note the drift. It’s a poor 10MHz OCXO
145GHz with Rubidium
  Note the short-term drift. This won’t work for narrow BW modes.
145GHz with lab grade 10MHz OCXO and Direct Synthesis
  Not too bad.

## Slide 28: 241GHz Station

## Slide 29: Close-up of 241GHz Dish

## Slide 30: W4WWQ having fun

## Slide 31: It’s also about the WX
My new friend……the Skew-T plot
because surface dew point isn’t the whole story

## Slide 32: The Path

## Slide 33: The Reverse Path

## Slide 34: The QSO

## Slide 35: The Thanks
Virginia Diodes, Inc.
Charles Wenzel of Wenzel Associates
Tom Van Baak of Leapsecond.com
Bill Overstreet, K4AJ for PLL assistance
Pete Lascell, W4WWQ for playing Polar Bear and roving
and many more…..
More info at www.mgef.org
And now……..

## Slide 36: The Results!!!