## Slide 1: Experiences with CT1DMK Reflock Board
By
Wes Atchison
WA5TKU
10/16/2004

## Slide 2: Experiences with CT1DMK Reflock Board
CT1DMK Reflock Board

## Slide 3: Experiences with CT1DMK Reflock Board
Reference Lock
Lock a 50-150MHz VCXO to a 10MHz reference
1
2
F3
SMB
1 2
R2
100K
VCC
2 1
D1
BAS32
1
2
R3
1K0
VCC3
1
2
R11
1K0
1
2
R12
1K0
1
2
R13
1K0
VCC
1 2 J4
1 2 J5
1 2 J6
I/O 2
I/O 3
I/O 5
I/O 6
I/O 8
I/O 10
I/O 12
I/O 13
I/O 14
I/O 15
I/O 18
I/O 19
I/O 20
CK1 37
OE1 38
CLR 39
OE2/CK2 40
I/O 21
I/O 22
I/O 23
I/O 25
I/O 27
I/O 28
I/O 31
I/O 33
I/O 34
I/O 35
I/O 42
I/O 43
I/O 44
TDI 1
TMS 7
TCK 26
TDO 32
U2
EPM3064ATQ44
QFP44
1
2
R4
1K5
1
2
R5
1K0
1 2 J2
1 2 J1
2
3
1
Q1
BC847
1
2
C1
10n
1
2
R1
10K

## Slide 4: Experiences with CT1DMK Reflock Board
Jumper Settings
Install Jumper for ‘0”
  J4 - LSB
  J6 – MSB
VTune
  Up
  Down
  XOR

## Slide 5: Experiences with CT1DMK Reflock Board
Universal Version Jumper Table
J6 J5 J4
-- conf=000 locks to the nearest 10KHz multiple
-- conf=001 locks to the nearest 100KHz multiple
-- conf=010 locks to the nearest 2.5KHz multiple
-- conf=011 locks to the nearest 25KHz multiple
-- conf=100 locks to the nearest 3.3333...KHz multiple
-- conf=101 Locks to the nearest 33.33333...KHz multiple
-- conf=110 locks to the nearest 5KHz multiple
-- conf=111 locks to the nearest 50KHz multiple

## Slide 6: Experiences with CT1DMK Reflock Board
Problems Found
  Programming Cable
  Solder Shorts
  Voltage Regulator @ Current Limit
    Recommend Lower Input Voltage – 10 Volts
    WA5VJB 2nd Rev Board with Holes for 7805 Tab Package (TO-220)

## Slide 7: Experiences with CT1DMK Reflock Board
Problems Found cont.
  Grounding of Ref Lock Board & Frequency West Source
  Check Level & Jitter of Reference Oscillator
    Look @ Input of FPGA
    Changed Resistors and Caps on 74F04
      Made C3 & C4 same as C5 & C6
      Made R6 & R7 same as R8 & R9

## Slide 8: Experiences with CT1DMK Reflock Board
Problems Found cont.
  Check Level & Jitter of VCXO
    Look @ Input to FPGA
  Check Level & Jitter of VTune
    Added 27K Resistor in Series with 10 uf Capacitor to Ground
    Reduced Jitter
    Additional Work on Loop Filter Needed

## Slide 9: Experiences with CT1DMK Reflock Board
Problems Found cont.
  Oscillator Needs to be Stable Stand Alone
  Range of VTune Must be Matched with Tune Range of Oscillator

## Slide 10: Experiences with CT1DMK Reflock Board
Experience with Universal Program
  Placed Adjustable P/S on VTune Input to FW Source
  Characterize VTune Frequency Response
  Set Frequency of Oscillator with VTune @ Center of Range ~2.5 Volts
  Check Oscillator Frequency for Lock

## Slide 11: Experiences with CT1DMK Reflock Board
Frequency West Brick Modification

## Slide 12: Experiences with CT1DMK Reflock Board
Frequency West Brick Modification

## Slide 13: Experiences with CT1DMK Reflock Board
Drive Levels
  10 MHz Reference - ~ 4.3 V pk-pk
  Not 50 ohm input
  Solid Trace Ground

## Slide 14: Experiences with CT1DMK Reflock Board
VCXO Output - 93.6 MHz - ~ 3.6 V pk-pk
  Not 50 ohm input
  Solid Trace Ground

## Slide 15: Experiences with CT1DMK Reflock Board
VTune - 1 Volt/Div - 5 ms/Div
  Level & Frequency Vary with Lock
  Solid Trace Ground

## Slide 16: Experiences with CT1DMK Reflock Board
10 MHz Reference Oscillator Phase Noise
  -117 dBC/Hz @ 10 KHz
  EG&G Cinox Oscillator
  Foam Box to Reduce Temperature Drift

## Slide 17: Experiences with CT1DMK Reflock Board
Frequency West Source LO
  93.6 MHz Oscillator Locked to 10 MHz Reference
  -118 dBC/Hz @ 10 KHz

## Slide 18: Experiences with CT1DMK Reflock Board
Frequency West Source NOT Locked to 10 MHz Reference
  Cleaner 5616 MHz Signal
  -113.8 dBC/Hz @ 10 KHz Phase Noise

## Slide 19: Experiences with CT1DMK Reflock Board
Frequency West Source Locked to 10 MHz Reference
  -111 dBC/Hz @ 10 KHz
  5616 MHz Wide
  Due to 2 VCOs Locked with Different PLLs?

## Slide 20: Experiences with CT1DMK Reflock Board
Frequency West Brick DMK Locked to Z3801
  -110.8 dBC/Hz @ 10 KHz
  No Difference

## Slide 21: Experiences with CT1DMK Reflock Board
Frequency West Brick DMK Locked to Shera Ref
  -110.7 dBC/Hz @ 10 KHz
  Little Difference

## Slide 22: Experiences with CT1DMK Reflock Board
Frequency West Brick Unmodified
  - 103 dBC/Hz @ 10 KHz

## Slide 23: Experiences with CT1DMK Reflock Board
Summary
  Additional Work on Loop Filter
  Understand What Level of Phase Noise is Adequate?
  On Air Testing
  Lock Frequency Stable
  Stable Basic Oscillator Required