## Slide 1
Extra Terrestrial LASER Communications:
Satellite and Lunar Laser Ranging
Paul Perryman, PhD
WA5WCP
paul.perryman@lmco.com

## Slide 2
Paul Perryman: WA5WCP
First Licensed: WN5WCP in 1968 15m cw
Areas of interest: HF, VHF, UHF, EME
First laser experience: 1970 : HeNe open frame, mw
Laser Systems I have known:
Nd: Glass Modelocked 6 ps, 105 watts Peak
Nd:YAG 10 ns Military Target Designator / Rangefinder
- 100 mj to 1 j per pulse
Ruby – Q- Switched, multi j
Argon Gas cw ; 10 w
CO2 : 1 w to 11 kw cw
Nitrogen home brew: 10 ns, kw peak
Er: Glass Eyesafe rangefinding
Employed by: Texas Inst, VARO, General Dynamics Land Systems, Lockheed Martin MMFC: building sights, sensors, and fire control on military platforms since 1988: C-130, Abrams M1, F15, F16, JSF, ABL

## Slide 3
Extra Terrestrial LASER Communications
Satellite and Lunar Laser Ranging
- Introduction: History and Examples
- List of Current Targets
- Lunar Laser Ranging Fundamental Ideas
- Safety Issues and Concerns
- Conclusion and Recommendations
- References and Web Links
Get a Familiarity with Laser Terminology and Concepts:
Enough Numbers to Provoke
- Where Do We Go From Here?

## Slide 4
Electromagnetic Spectrum

## Slide 5
Introduction: History and Examples
When | Who | Laser | Energy (pulsed) | Xmit | Rcv | div (deg)
May 1962 | MIT Labs | Ruby | 50 j | 12 in | 48 in | 1.15E-02
1997 | ? | Nd:YAG 2x | 10 J @ 15hz | 3.2 in |  | 
Current | McDonald Observatory | Nd:YAG 2x | 1.5 J @ 10 hz | 30 in | 30 in | 4.30E-06
Lunar Laser Ranging (LLR)
Satellite Laser Ranging (SLR)

## Slide 6
Current Targets: Lunar and Satellite Reflectors
Apollo Retro Reflectors: 11, 14, 15 (1969, 1971)
Lunakhod 2
Forty Earth Orbiting Satellites with Retro Reflectors:
GPS 35,36 - Stella
Glanass 68,71 - AJISAT
LAGEOS 1,11 - Meteor 2,3
ERS-2 - Westpac
GEOS -2 - ETALON -1

## Slide 7
Optical Retro Reflectors : Corner Cube
100 to 300 Fused Silica Cubes: 3.8 cm in dia

## Slide 8
Essential Ideas for Lunar Laser Ranging
Laser Source : Pulsed is better than CW (Q-Switched YAG)
  Ex: Q-Switched Nd:YAG 20 nsec pulse width
  100 urad (0.006 deg) divergence (Full angle beam width)
Pointing and Tracking : Needs to be as good or better than the Divergence of Laser ( 0.0006 deg or 10urad)
- Telescope stability ~ 0.4 arc sec = 2 urad
- Target is 0.003 urad
Propagation:
  Absorption and Scattering
  Atmospheric Bending, Turbulence (“seeing” varies by 1000x)
- Launch and Recovery: Big Optics with Very Stable Mount ( Diameter 24 inches or more) : Internal Fire, Optically Induced Damage?
- Receiver: Solid State Detectors continue to improve (10’s of nw sensitivity currently available)

## Slide 9
Atmospheric Loss

## Slide 10
Conceptual Radar Range Equation
Distance
Relative Signal Level
Xmtr
Launch Antenna / Optics Gain
Atmospheric Scatter, Turb, Abs
100 miles
285k miles
1 ‘
(Distance)
2
Geometric Target OverFill Loss, Reflectivity
1 ‘
(Distance)
2
Receive Antenna , Optics Gain Polarization Mismatch
Atmospheric Scatter, Turb, Abs
285k miles
100 miles
Rcvr
Moon

## Slide 11
So What Happens if You Just Try Something?
- Surplus Laser ( HamCom, Dayton or ??) Nd:YAG 100 mj per pulse Q-swi, 20 hz, Peak power density is 100s of kw / cm^2
- Big Telescope : 18 to 20 inches
- Get a State-of-the-Art Rcvr Chip for Detection : 200 nw sensitivity
Lash it up and see what happens:
Pointing stability is probably not near good enough to get enough power on target
May optically damage the telescope
Working thru the Radar Range Equation for Lasers shows a large negative S/N best case
AND: what are the other “side issues”?
Acquire the Equipment:

## Slide 12
Safety Issues and Concerns
Eye Hazards : The Eye is a VERY sensitive Receiver!
  Damage possible even to invisible radiation
  Damage to Cornea or Retina
  Damage to Skin
- The Nominal Eye Hazard Distance: (EHD) What is the closest distance for intra-beam Viewing that is considered safe?
- Depends on:
  Laser Wavelength, Power Level, Pulsed or CW (Laser Class)
  Atmospheric Conditions
  Any Visual Aids for the Eyes? (i.e., Binoculars)
- Many Accidents / Injuries around Lasers are not Optical but Electrical !
- American National Standards Institute (ANSI Z136) : The Standard for Eye Safety Levels

## Slide 13: Eye Hazards by Laser Classification
Class I – Exempt: Normally the Eye Hazard Distance is zero
Class II – Normal Eye Avoidance Response (<0.25 sec) will prevent damage, extended direct viewing can exceed Maximum Permitted Exposure (MPE), but staring or powered optics is risky!
Class llla – Controlled: Eye avoidance may save your eye, but not guaranteed: powered optics and extended exposure is very risky
Class IIIb – Controlled: Eye avoidance is not good enough for direct or Specular reflections => permanent damage is possible
Class IV – Controlled: Direct, Specular, or Diffuse reflections are very dangerous: permanent eye damage, fires (> 2 W/cm^2)
ANSI Standard Z-136.1-1993

## Slide 14: What are the Technical Specifications For Each Laser Class ? (visible and near visible : 400 nm to 1100 nm)
Class One: power output less than 0.4 µW for CW lasers
Class Two: (400 - 700 nm) and have power outputs between 0.4 µW and 1 mW for CW lasers
Class Three:
  3a: Power outputs for Continuous Wave (CW) lasers operating in the visible range are between 1 - 5 mW. Blink will probably save you, but power optics is bad
  3b: 5 - 500 mW for CW lasers
Class Four: > 500 mw and most pulsed lasers

## Slide 15
Safety Issues and Concerns
- The FCC says ALL above 300 Ghz BUT: Outdoor Laser “Displays” are governed by more that one agency!
- Governing Agencies for Un-terminated Beams (Laser Light Show):
-- FDA: Center For Devices and Radiological Health (CDRH)
-- Occupational Safety and Health Administration (OSHA)
-- Texas Bureau of Radiation Control or your state’s equivalent
-- FAA
-- Local
Legal Issues:
What is the Risk? : Injury, and or Money changes hands
So what is a Laser based accident like?
  - He Ne: 0.1 to 1 milliwatt cw
  - Military Rangefinder at Dayton (EHD km)
  - 25 Kv times a pf / ft
  - Death of a Design Engineer
Bottom Line: Risks can be Comparable to the large EME stations: but Very different !

## Slide 16
16 May 2004 Dayton Hamvention – Surplus Laser

## Slide 17
Dayton 2004 – Litton Military Target Designator / Rangefinder
100mj / pulse, 1.06 um, 20 hz : EHD >10km

## Slide 18
Where Do We Go From Here:
Are There No Amateur Laser Comms in the Future?
Whether you are having Ideas about Laser EME or are interested in setting new optical wavelength distance records:
  The technical difficulty of Brute Force Laser EME is very great: Getting a bright enough source to do the problem, and pointing and tracking are currently the domain of government and University groups.
  The many government and legal requirements should all be considered: Federal, State, Local
  The safety issues must all be considered: (i.e., What is the Eye Hazard Distance?)
  So What is the Best Plan for Laser Technological Advancement for the Amateur Radio Community?

## Slide 19
Conclusion and Recommendations
The Challenge will be to blend the Extreme Bandwidth with Novel Modulation / Encoding and Detection Schemes so:
    Time Domain, Polarization, Frequency Domain Modulation
- The Big Advances in Computing Will Allow Significant Improvement in Detection (ex: Regenerative Det)
- Peak and Average Power can be Low within Safe Limits
The Carrier Frequency of 474 Thz will Allow Huge (ie.,300 Ghz) Sidebands!
Extraterrestrial : Who knows where this will lead?
Who will be the first to have a 144Mhz, 432Mhz
or 10 Ghz Laser Plus Rf IF Contact?

## Slide 20
Optical Versions of RF Technology
Oscillator Laser
Amplifier Optical Amplifier
Detector Photodetector (photodiode, avalanche)
Mixer Optical Mixer : Non Linear Crystals
Parametric Osc, Amp Optical PO, or OPA
Feed Line Fiber Optics
Rf
Optical

## Slide 21
Example: Optical Heterodyne Detector
Lens
Photo
Detector
Laser – Local Oscillator
Signal
IF at Rf
Detector / Receiver
F
F
F + F
F - F
sig
Lo
sig
sig
Lo
Lo
Beam Splitter

## Slide 22
Conclusion and Recommendations
Recommendation: That all Contests and Records from now on ONLY consider Class I laser sources
OR
All Contest Entries and Claimed Records Must Have Complete CDRH, FAA, State, and Local Compliance
Recommendation: To Encourage Technology Awareness in the Amateur Community, Give Bigger Incentives in the Contests and Records for Laser Beyond Direct Detection and Simple On-Off Modulation contacts.

## Slide 23
References and Web Links:
- K3PGP : www.k3pgp.org
- N9JIM : www.qsl.net/wb9ajz/laser/laser.htm
- Federal Regs: http://www.fda.gov/cdrh/comp/eprc.html
- State of Texas Regs: http://www.tdh.state.tx.us/radiation/laser.htm :
- McDonald Observatory: http://www.csr.utexas.edu/mlrs/dda.html
- SLR and LLR: http://cddisa.gsfc.nasa.gov/slr_summary.html
- http://geophysics.ou.edu/solid_earth/readings/apollo_laser_ranging.html
- www.powertechnology.com/TECHLIB/SAFETY.ASP
- www.laserfaq.org/

## Slide 24: Appendix : Units of Optical Measurement
Transmitter Power : Peak Power : KiloWatts , MegaWatts
Receiver Sensitivity : NanoWatts
Angular : Milliradian, Microradian :
- (360 degrees/ 2*pi radians)=
57 degrees / radian
- .057 degrees / millirad
- .000057 degrees / microradian
And For Arcsec = (360 * 60 *60 arc sec / 2*pi rad * 10^6) =
0.2 arcsec = 1 urad
Pulse Width : Nanoseconds