## Slide 1: 122 GHz DB6NT Mixer
W5LUA
May 2, 2020

## Slide 2: Various DB6NT PCBs

## Slide 3: Drilling Housing for WR-12 and WR-06 Waveguide Flanges
I had several pre-machined housings (left) that I decided to modify (right) for use with the 120 GHz DB6NT mixer boards
61 GHz LO input waveguide
122 GHz RF port
Fc = 115 GHz

## Slide 4: Using Granite Surface Plate and Digital Height Gage to scribe lines
https://www.grizzly.com

## Slide 5: DB6NT 122 GHz Mixer PCB
Piece of acrylic plastic drilled to match holes in housing.
Provides a drilling template for pcb and
will be used to apply pressure on board when silver
epoxying board into place.
Shining a flashlight into the RF and LO ports gives a good indication of alignment with pcb.
Next step is to make back shorts for LO and RF ports
PCB #40

## Slide 6: LO and RF Back Shorts
61 GHz LO Back short
122 GHz RF Back short
4-40 tuning screw
0-80 tuning screw

## Slide 7: DB6NT 122 GHz Mixer
Completed mechanical assembly
Looking down towards 61 GHz LO input
Looking down towards 122 GHz RF port
IF
LO
RF
DC Bias

## Slide 8: Next Step
Silver epoxy PCB into housing (or not)
Wire IF port and dc port
Install Diodes
Test

## Slide 9: MA4E1318 Anti-Parallel Flip Chip Diode Pair
Cost per diode only $2.17 from Mouser but you must buy in 100 quantity

## Slide 10: MG Chemicals 9400 Electrically Conductive Adhesive
One-part Epoxy
Recommended for semiconductor attachment.
Unlimited working life
Store in freezer
Heat Cure 70C (158F) for 2 hours.
Now for the fun……not

## Slide 11: Installing the Diode
I decided NOT to epoxy the pcb in place.
I will rely on the LO and RF back shorts to keep the pcb in intimate contact with the housing.
I built a bracket to keep pcb in close contact with the housing when the RF back short is removed.
I had tremendous difficulty in keeping the epoxy away from the LPF.
I decided to use regular clear tape to mask off area where I did not want to have epoxy, then remove tape and put diode in place.

## Slide 12: Diode Pair Installed
Diode installed
Only ruined or lost 5 diodes!

## Slide 13: Toaster Oven for Curing Epoxy
July 7, 1973 Wedding Present
Heat Cure 70C (158F) for 2 hours.

## Slide 14: Testing the Mixer
I have no test equipment for 122 GHz, so in the true ham spirit, I must improvise.
Most importantly, I need a signal source at 122 GHz.
Need to accurately measure receive dBs so I can tune for the last dB.. I use NaP3 Power SDR software with my K3 & DEMI 2m XVTR.
Now back to making a signal at 122 GHz..

## Slide 15: Potential Weak Signal Sources for 122 GHz
ST Microwave Amplifier/Multiplier heard on 47/76 GHz
60 GHz WR-15
Amplifier
60 GHz X4 Multiplier
Wiltron 13 to 20 GHz Amplifier & Spacek X3 (U-3X) with WR-22 output. Converted WR-22 to WR-15 & WR-15 Horn supplied by K9JHK, Thanks Karl!
CMA 382400 39 GHz X3 mult & 76 GHz SHM

## Slide 16: 122 GHz LO & IF Sections
ZL2BKC 14 GHz PLL
Avago AMMP-6120 8-24 GHz X2 Multiplier
DEMI TC IF Interface with PGA-103 LNA (less than 1 dB NF)
Millitech X4 Multiplier Pout =10 dBm
7632 MHz
61056 MHz
15264 MHz

## Slide 17: Front Panel of 122-134-241 GHz Transverter

## Slide 18: Test Bench for tuning up mixer

## Slide 19: 122,256.1 MHz
Most phase noise is due to multiplying the HP8340A 15282.0125 MHz signal X8
Near-in spurs are -25dBc, still sounds T8+

## Slide 20: Completed 122 GHz System

## Slide 21: 12” Cassegrain Fed Dish on 122 GHz
Mark N0IO used the W1GHZ Cassegrain Calculator to find the optimum feed and sub reflector for my 39 GHz dish. Mark machined both pieces. A big thank you Mark!

## Slide 22: Closeup of mixer & transition to circular waveguide to dish feed

## Slide 23: W2IMU Feed & Cassegrain Reflector

## Slide 24: Summary
Hope to work you on 122256.1 MHz
Any questions?