## Slide 1: Microcontrol of Microwave Stations
Copyright © 2006 – Stephen Hicks, N5AC
All Rights Reserved
There’s nothing that can’t be done
with Velcro and microprocessors
Stephen Hicks — N5AC, AFA4SH

## Slide 2: Agenda
Copyright © 2006 – Stephen Hicks, N5AC
All Rights Reserved
What’s there to control?
How control is achieved
Common control methods
Control hardware tradeoffs
The sky’s the limit – novel applications
Typical practical applications

## Slide 3: What’s there to control?
Radios – most modern have serial inputs
  Retrieve operational data
  Alter operational parameters such as frequency
Transverters – all have a PTT line to control
Switches – switching of one IF rig to multiple transverters
Sequencing – switching in-line preamps, amplifiers at different times in a QSO
Power supplies – for efficiency, protection, etc. may want to enable and disable various supplies
System transmit – may want to lock-out transmit in unsafe situations

## Slide 4: Basics of control
Basic types of control
  Output Binary: switching something on or off
    PTT line of a transverter
    Switching a PA on or off
    Switching a transfer relay
  Output Data: control of a device such as a radio with frequency information
  Input Binary: sense microphone PTT pressed
  Input Data: read S-meter or mode in radio

## Slide 5: Binary Output
Often handled with a relay or a bipolar transistor
Oh, and you generally need a transistor to switch the relay!

## Slide 6: Binary Output Comparison
 | 2N2222 | relay
IC | 600 mA nom | unlimited
TSAT | 25ns | 5-10ms typ
Operations | billions | 100,000 typ
Cost | 6-40¢ | $0.50-10.00

## Slide 7: Control Hardware
Switches
Just relays
  Simple and effective
  “programming” often achieved with wiring or jumpers (DEMI / W5LUA sequencer)
TTL/CMOS logic
  Cumbersome, rarely implemented, difficult to adjust
µContoller
  Flexible
  Programmed with assembler, BASIC, C languages
Computer
  Integrated with station, perhaps (work with logger)
  Programmed in any number of languages
Combinations
  SDR software to relay board, for example

## Slide 8: Sequencers
Input signals, generally a PTT, cause a cascade of timed relays to enable and disable preamps, power amplifiers and the like
Corresponding “unwind” on release of PTT
Generally, need one sequencer per band
Only offers one sequence as wired (variability achieved off-line with wiring)
Simple and reliable

## Slide 9: Computer Control
Generally achieved via parallel port on computer, but IEEE-488 and serial also options
A number of logging programs have been adapted to use this method
Limited to 8 or so outputs without logic
Requires a computer, obviously
Programming required

## Slide 10: µController
Widely available and inexpensive
Easy to interface
Often have on-board serial, display drivers, etc for advanced projects
Can be programmed in assembler (yuk), C or BASIC

## Slide 11: Common µControllers
PIC made by Microchip probably #1 in sales
  Comes in LOTS of different sizes, shapes, configurations
  Target across the board, but many sold into commercial embedded applications
BASIC stamp by Parallax sold gobs also
  Target is generally educational market and hobbyists, but commercial path exists also
Others
  Rabbit, Freescale (formerly Motorola), Fairchild, Zilog, etc.

## Slide 12: On Languages
I find I have to defend using BASIC on a regular basis
  I first programmed a computer at age 12 in BASIC
  I wrote my first 6502 assembler program (a contest callsign deduper) at age 14
  I have been a software engineer for many years and I am comfortable writing in over a dozen programming languages including several assemblers …
So why BASIC??

## Slide 13: On Languages …
Who uses BASIC anymore anyway??
  ASP[x], the most common web language on the Internet is a derivative of BASIC
  PHP, Perl, and many other web and scripting languages are derivatives of BASIC’s dynamic typing and simple coding
BASIC hides a lot of the complexities of programming like memory allocation and type casting

## Slide 14: What do you gain?
TIME TO MARKET
Ease of development and debugging
Later readability of code
“layman” more likely to be able to read and understand your code
Large enhancements and modifications, even in the field, are easy

## Slide 15: Programmability Example
In January 06 VHF SS, I had a control system on a BASIC stamp® connected to a LCD display
The display failed and I lost positive control of my entire µW system
I reprogrammed the controller to take inputs on the serial port from my laptop in about 20 minutes
FRANKLY, NOT POSSIBLE IN ASSEMBLER

## Slide 16: What do you give up?
BASIC is somewhat less “deliberate” since things are done for you
  You might find that variables you send out a serial port aren’t in the format you want
You may lose interrupt control
  Not terribly important for out application
  Polling is a good alternative
BASIC often requires more memory
  Hey, we’re not writing a database app here … memory is plentiful today

## Slide 17: In the end…
Which platform and language you use will be a matter of personal comfort and interest
If you are new to programming and microcontrollers, I recommend the BASIC Stamp®
If you need flexibility and are willing to pay for it with development time or you are going to release something commercially and need low cost/part, get a PIC
If you need the ultimate in power and flexibility and are willing to pay for it with $$ and time, get a Freescale processor

## Slide 18: Getting Started with BASIC Stamps®
What you need
  A BASIC Stamp Module such as a BS2p, BS2p40 or development board
  A power supply
  A computer with a serial port (or USB-serial adapter) [some BASIC Stamp boards use USB]

## Slide 19: BASIC Stamp comparisons
BASIC Stamp 2 has a PIC 16C57 with EEPROM, oscillator, serial interface, etc.
$49 in quantity one
Processor Speed | 20 MHz
Program Execution Speed | ~4,000 instructions/sec.
RAM Size | 32 Bytes (6 I/O, 26 Variable)
EEPROM (Program) Size | 2K Bytes, ~500 instructions
I/O Pins | 16 +2 Dedicated Serial
Voltage Requirements | 5 - 15 vdc
Current Draw at 5V | 3 mA Run / 50 µA Sleep
PBASIC Commands | 42
Size | 1.2"x0.6"x0.4"

## Slide 20: BASIC Stamp comparisons
BASIC Stamp 2p40 has a UBICOM SX48 with EEPROM, oscillator, serial interface, etc.
$79 in quantity one
Processor Speed | 20 MHz Turbo
Program Execution Speed | ~12,000 instructions/sec.
RAM Size | 38 Bytes (12 I/O, 26 Variable)
Scratch Pad RAM | 128 Bytes
EEPROM (Program) Size | 8 x 2K Bytes, ~4,000 instructions
I/O Pins | 32 +2 Dedicated Serial
Voltage Requirements | 5 - 12 vdc
Current Draw at 5V | 40 mA Run / 350 µA Sleep
PBASIC Commands | 61
Size | 2.1"x0.6"x0.4"

## Slide 21: Development Boards
Fairly self explanatory
Basics are:
  Power the part
  Provide serial connector to program
  Provide breadboarding area for experimentation
  Additional components, input/output devices
Range from $25-$250

## Slide 22: “Board of Education”
For BS2 only, $65 qty one
What it has
  Small breadboard area
  Regulator
  Driver for servos (for turning 24GHz horns?)
  Serial connector for programming

## Slide 23: BS2p24/40 Demo Board
$89 quantity one [not incl stamp]
Breadboard area
Supports BS2p24, BS2p40
On board 5v regulator, serial connector, switch, pot, etc

## Slide 24: Professional Development Board
$149 quantity one
What it has
  Loads of switches
  5-digit 7-seg LED displays
  Speaker
  socket for any BASIC stamp
  16 blue LEDs
  Large breadboard area
  Etc…

## Slide 25: BASIC Stamp Development Environment

## Slide 26: Control with the BASIC Stamp®
Keying a transverter
To key the transmitter
  HIGH PIN1
To unkey the transmitter
  LOW PIN1
It’s that simple!

## Slide 27: Input with BASIC Stamp
Connect input to input pin (iPTT)
  iPTT PIN 4 ' input pin #4 for PTT request
  lastTXstate CON $07A ' last transmit state
  GET lastTXstate, x ' get the PTT state the last time here
  IF iPTT = x THEN RETURN ' no need to do anything (same)
  PUT lastTXstate, iPTT ' save our tx state for next time
  IF iPTT = 1 THEN ' no key down (float high)?
  GOSUB sequenceOff ' no PTT, make sure we aren’t TXing!
  ELSE ' we're key down, so
  GOSUB sequenceOn ' Transmit !
  ENDIF

## Slide 28: Running a program
After you type your program in the development environment, just press “play”
  Your code is downloaded into the EEPROM on board the BASIC Stamp
  Your program is executed
  Pressing the reset button will restart your program and run it again

## Slide 29: Working inside boundaries
Limited memory: 26 bytes of RAM, program in blocks of 2048 bytes, 128 bytes of EEPROM scratchpad

## Slide 30: Boundaries …
You learn to keep only important things in RAM
Learn to use several “scratch” RAM locations over and over
  load EEPROM data into RAM for manipulation
  store back in EEPROM later
Programs that grow over 2K (tokenized) have to be segmented across program memory

## Slide 31: Sequencing
' -------------------------------------------------------------------------
' sequence transverter/transmitter operation
' -------------------------------------------------------------------------
sequenceOn:
GET curBandPTT, x ' get the pin # for current band’s PTT line
IF x <> 0 THEN ' if we're using a transverter, let's key it
OUTH = x ' transmit on this transverter
PAUSE 50 ' let the transverter key down (10ms)
ENDIF
HIGH oPTT ' key the IF rig
RETURN
OUTH sets all outputs to value x … in this case it is just the bit for the single PTT line .. For example x=4 for bit #2, x=8 for bit #3

## Slide 32: Reading radio frequency
SEROUT Radio1Out, Radio1Baud, [$00,$00,$00,$00,$03]
SERIN Radio1In, Radio1Baud, 500, NoRadioData, [STR rdata\5]
IF (rdata(0) > $99) OR (rdata(2) > $99) OR (rdata(3) > $99) OR (rdata(4) > $99) THEN GOTO NoRadioData
freq(0) = (rdata(3) & $0F) + ((rdata(3) & $F0)>>4 * 10)
freq(1) = (rdata(2) & $0F) + ((rdata(2) & $F0)>>4 * 10) + ((rdata(1) & $0F)*100)
freq(2) = (rdata(1) & $F0)>>4 + ((rdata(0) & $0F) * 10) + ((rdata(0) & $F0)>>4 * 100)
freq(3) = 0
DEBUG "[RADI] ",DEC freq(3),DEC3 freq(2), ".", DEC3 freq(1), ".", DEC2 freq(0) ,CR
This is for a Yaesu, but most radios will be similar … you could even have different code for each radio!

## Slide 33: Setting Radio Frequency
' -------------------------------------------------------------------------
' SetFrequency - Set Radio Freq after band change
' -------------------------------------------------------------------------
SetFrequency:
GET curFreq,y ' get our current band (1=6m, etc)
GET y,x ' get last freq from last time this band
SEROUT Radio1Out, Radio1Baud, [x]
GET y+1,x
SEROUT Radio1Out, Radio1Baud, [x]
GET y+2,x
SEROUT Radio1Out, Radio1Baud, [x]
GET y+3,x
SEROUT Radio1Out, Radio1Baud, [x, $01] ' Set freq on radio
GET y+4,x ' Get last antenna
PUT CurBandAnt, x ' Store antenna locally
RETURN

## Slide 34: Other things …
You can read and set mode of the radio
  You could increase delays for FM or even prevent FM operation
  You could limit the transmit time on FM
You could put up a button on a display labeled “DASHES” when in CW and then when it is pressed, you could ground the keyer dash input of the radio…
You could measure the temp of your PA and light a warning light if it is hot … or disable transmit … or bypass the PA!
You could scan beacon frequencies, read the S-meter of the radio and send an email when the beacon appears or is above a specified S-meter reading

## Slide 35: More Things…
Turn a TIB on and off to regulate power to the IF rig
Electrically “move” a single keyer between multiple radios
Switch a single microphone between bands
Switch antenna configurations
The sky is the limit …

## Slide 36: The Hardest Part
As you can see, getting inputs and outputs and manipulating everything is fairly easy
User interface is harder…
Generally separate from the actual control logic board

## Slide 37: Control System
Copyright © 2006 – Stephen Hicks, N5AC
All Rights Reserved
BASIC stamp 2P40
2N2222 to control all PTTs and relays
28V impulse for relays
Serial to radio & display
DB25 to all PTTs, relays
A few kLOC of PBASIC

## Slide 38: User Interface Options
Stand-alone display
Computer terminal program
Computer display program
LCD display
Your IF radio (!)
Others …

## Slide 39: My thoughts on UI
I don’t like big in the mobile
I like LCD display – they look clean and are small and lightweight
I am beginning to think I might like the computer best of all
I’m indecisive at best … I think I’m going to try each one once before making a decision!

## Slide 40: LCD display
Self contained and convenient
Can be used for both input and output and can be very flexible
Still working to keep RF out of it
Otherwise this is one of my favorites

## Slide 41: Touch Screen Control
Copyright © 2006 – Stephen Hicks, N5AC
All Rights Reserved

## Slide 42: Touch Screen Control
Copyright © 2006 – Stephen Hicks, N5AC
All Rights Reserved
Band switch with touch of a “button”
Remembers last frequency used on each band
Shows actual TX/RX frequency
Controls TIB, Transverters, PTT of radio
One touch to go to calling frequency on band
BIG for mobile use and harder to keep running in an auto

## Slide 43: Computer Display
Probably the most flexible of all
Requires some programming skills on the PC as well as the µC
My next project is to integrate control system with the PC
I’ll probably use two RS-232 ports at the same time – one for control via a logger and one for status display to code that I write

## Slide 44: Next Steps
I’m working on a generalized PCB for use as a µW controller
The idea is to make a board that takes a couple of different microcontrollers and has jumpers for configurable input/out
These are my thoughts:
  A couple of 28v control circuits for relays
  Up to three serial ports with connectors
  Most I/O pins as either input or output
  Drivers for output pins
  Perhaps space to use relays in addition to transistor drivers if so desired

## Slide 45: Questions?
Copyright © 2006 – Stephen Hicks, N5AC
All Rights Reserved