## Slide 1: The Shera Lockbox revisited”
Dave Robinson WW2R

## Slide 2: Original Design
Original Article published in QST July 1998 37-43
Principal of operation:-
A one pulse per second signal available from the GPS receiver is phase compared with the 10 MHz reference by using a gated oscillator and a counter. An error voltage generated by this comparison is used to fine tune the 10MHz reference frequency. The comparison and filtering is done digitally in a PIC microcontroller.

## Slide 3: First Model
Built Late 1998, written up and presented at Update 1999 http://users3.ev1.net/~g4fre/update99.htm

## Slide 4: Early Results
Never totally happy with it:-
Oscillator needed resetting (drift)
Box got Very hot
Only one output which was load sensitive
At this point the HP Z3801 10MHz lockbox started appearing on the surplus market so after getting one of these the Shera was shelved

## Slide 5: W7CQ
Browsing the Internet I came across the W7CQ web site with a writeup of how he interfaced the Shera to an HP10544 Oscillator.
http://home.teleport.com/~oldaker/10mhz_construction.htm
Interest in Shera re-kindled!

## Slide 6: Oscillator Mounting
The first thing obviously needed was to put the Oscillator in a separate thermally Insulated box

## Slide 7: Power Supply
Old Configuration: One transformer was used providing +28V (for oscillator heater) and all regulators were fed by this some of which were dropping 16 and 23V: Much dissipation, much heat even when mounting the regulators off the board on the chassis.
New Configuration: Searching Junk Box (and a visit to Tanners) produced 2 transformers which would fit in box. One provided 18V which when bridge rectified provided 28V for the oscillator heater
The Other provided 12V CT which using 2 diodes produced 16V for the 12V and 5V regulators
G3TGE:-
”99% of all problems are PSU related”

## Slide 8: Outcome
With these changes the box was set up aligned and the results were very good
Just needed to add more outputs

## Slide 9: Output Buffer
3 output SMT buffer published in Weinheim Proceedings 2000 by DC8ES. Also provides a TTL 10 or 5 or 1MHz output. Needs 12 and 5V.
I Built one on 1/8” DS PCB!

## Slide 10: Output Buffer
3 output SMT buffer published in Weinheim Proceedings 2000 by DC8ES. Also provides a TTL 10 or 5 or 1MHz output. Needs 12 and 5V.
I Built one on 1/8” DS PCB!
When the buffer was connected to oscillator Box lost lock!
Many solutions were tried over many days:-
FET buffer
Op Amp buffer
Feeding buffer circuit from a battery
No success

## Slide 11: Problem Resolved
Looking again at the Shera notes http://www.rt66.com/~shera/setup_notes.html
I came across a problem that wasn’t exactly like mine but anything was worth a try. The problem described was eventually diagnosed as “The VCXO signal becomes contaminated with a divided-down version of itself” Fix: 10pF across R2
Cured the problem instantly; now have three 10MHz outputs all around 1V

## Slide 12: Finished Unit

## Slide 13: Results
The Shera box has 7 modes, each of which has a different averaging period
N=2 1500s (~25mins)
N=3 3000S (~50mins)
N=4 6000S (~1h40mins)
N=5 12000S (~3h20mins)
N=6 24000S (~6h40mins
N=7 48000S (~13h20mins)
This is the time that the PLL takes to fully recover from a transient

## Slide 14: Mode 3

## Slide 15: Mode 5

## Slide 16: Mode 6 (2003)

## Slide 17: Mode 6 (2004)