## Slide 1: Tracking Microwave Rovers with APRS
By Bob Kmak
K5WO

## Slide 2: Keeping Track of Where Everyone Is
Recent NTMS events have been characterized by more rovers than home stations. Keeping track of where all the rovers are, especially when they are en route to a new location, has become increasingly difficult.

## Slide 3: Why APRS?
APRS is an automated method of broadcasting position, direction, and velocity data from an amateur radio station.
APRS-enabled rovers would continually broadcast their position via packet radio on 144.39 MHz.
Home stations monitoring APRS data either through the internet or using only radio could see the position of most or all rovers at any given time.

## Slide 4: APRS Review
In the US, APRS stations beacon on 144.39 MHz
The three basic components of an APRS beaconing station are a GPS receiver, 2 meter FM radio, and a Terminal Node Controller (TNC)
GPS
Radio
NMEA Data
TNC
PTT
XMT
RCV
Beaconing (rover) station

## Slide 5
An APRS monitoring station requires a computer and appropriate software for viewing the position of other APRS stations.
Computer
TNC
RS-232
Radio
PTT
XMT
RCV
Computer
Internet
Monitoring (home) station

## Slide 7
How APRS packets are propagated
Direct propagation from one station to another
Digipeaters - A number of stations in the area are configured to repeat, or retransmit, every packet they hear. The number of times a packet is digipeated is controlled by routing instructions embedded in the packet.
Internet Gateways - Some APRS stations are connected to the internet, and send all packets they receive to databases on the internet.

## Slide 8
The Tiny Tracker
A tiny, transmit only TNC.
Connects to transceiver and GPS receiver.
Can be configured to beacon only when moving, every X seconds, only when speed is above Y, etc.
$36.00 in kit form.

## Slide 9
Tiny Tracker configuration

## Slide 10: Configuring ‘Smart Beaconing’
SmartBeaconing Slow Speed, Slow Rate
This setting sets the SmartBeaconing slow speed (MPH) and rate (seconds). Speeds slower than the slow speed will cause TinyTrak3 to beacon at the Slow Rate.
SmartBeaconing Fast Speed, Fast Rate
This setting sets the SmartBeaconing fast speed (MPH) and rate (seconds). Speeds faster than the fast speed will cause TinyTrak3 to beacon at the Fast Rate. Fast Speed must be set higher than Slow Speed.
SmartBeaconing Min Turn Angle, Turn Slope, and Min Turn Time
These settings set CornerPegging parameters for the minimum turn angle (degrees), turn slope (MPH-degrees), and minimum turn time (seconds). Turns less than the minimum turn angle since the last transmission will not cause a transmission. The lower the turn slope, the quicker TinyTrak3 will transmit due to turning. Both Min Turn Time and Min Turn Angle must be less than 256.

## Slide 11: Monitoring APRS via the Internet
A web browser and internet connection are all that is necessary to monitor APRS data via the internet.
The most commonly used APRS website is www.findu.com .

## Slide 12: Querying APRS data

## Slide 13: Querying for N5 stations in the DFW area

## Slide 14: Map generated by query

## Slide 15: Querying by ZIPCODE

## Slide 16: APRS near Richardson

## Slide 17: Find U

## Slide 18: APRS software UI-View

## Slide 19: UI-View basic configurations
Use with hardware TNC
Use with soundcard TNC ( AGWPE )
Connect to internet

## Slide 20: References
Maps for APRS
http:/www.n5oom.org/2004_hamcom/presentations/maps_for_APRS.pps
Intro to UI-View
http:/www.n5oom.org/2004_hamcom/presentations/UI-View_presentation.pps
APRS Tracker Examples
http:/www.n5oom.org/2004_hamcom/presentations/APRS_Tracker_Examples.pps
Intro to APRS
http:/www.n5oom.org/2004_hamcom/presentations/Intro_to_APRS.pps

## Slide 21: References-continued
APRS for Emcomm & public service
http:/www.n5oom.org/2004_hamcom/presentations/APRS_for_Emcomm_and_Public_Service.pps
TinyTracker
http://www.byonics.com/tinytrak/
UI-View
http://welcome.to/uiview
Findu.com
http:/www.findu.com