## Slide 1: A 10/24GHz expedition to “East West Texas”
Dave Robinson WW2R

## Slide 2: Equipment
10GHz
IF: IC402 (435MHz) Demi xverter. Qualcom PA (1W) G3WDG preamp (0.9dB). 18” FSJ1 coax
24GHz
IF:IC402 (435MHz) Homemade DB6NT mixer. DB6NT preamp (2dB) Packratts PA (2.1W). 16” flexible WR-42

## Slide 3: 10G Transverter

## Slide 4: 24G Transverter

## Slide 5: W5ZN Dualband 10/24G feed
Using Dualband feed means if signal is peaked on 10G it will also be peaked on 24G

## Slide 6: Dish/Mount

## Slide 7: EM03XD Jacksboro

## Slide 8: EM03XD: roadside

## Slide 9: EM03XD towards W5LUA/AA5C

## Slide 10: EM03: Results
10GHz
Worked W5LUA 59 SSB EM13PC 125km
Worked AA5C 579 CW
Heard NT5NT/B 549 EM12PX 126km
24GHz
Worked W5LUA 57 SSB EM13PC 125km
No signals either way with AA5C

## Slide 11: EM03XD EM13PC

## Slide 12: EM02XS: Mineral Wells Airport

## Slide 13: EM02XS Roadside

## Slide 14: EM02XS: Mineral Wells Airport
N
E
S
W

## Slide 15: EM02XS: Towards W5LUA/AA5C

## Slide 16: Equipment mount

## Slide 17: EM02: Results
10GHz
Worked W5LUA 57 SSB EM13PC 130km
Failed to work AA5C but heard him 559 CW
Heard NT5NT/B 519 EM12PX 127km
24GHz
Worked W5LUA 559 CW EM13PC 130km

## Slide 18: EM02XS  EM13PC

## Slide 19: Lessons Learnt?
Always take a yagi for talkback. Just because others have made it on a loop does not mean you will as well.
Make sure when you take the FT817 apart you plug the speaker back in
If you have a kW generator don’t forget you can use amplifiers on talkback
Take a frequency reference/marker oscillator.