## Slide 1: Intro to Microwave Propagation for data
W5HN
North
Texas
Microwave
Society
NTMS
Joe Jurecka – N5PYK
North Texas Microwave Society

## Slide 2: Categories of microwave paths
Those who love propagation anomalies (Weak signal enthusiast)
Those who don’t (data link operators)

## Slide 3: Power Levels
For simplicity, links use dB and dBm to model performance
A relative change is measured in dB
dB=10 LOG (Relative intensity)
Specific levels measured in dBm
(dB referenced to a milliwatt)
With 802.11
-90 dBm weak
-50dBm strong
0dBm=1 mW
10dBm=10mW
20dBm=100mW
30dBm=1W
40dBm=10W
etc

## Slide 4: Free Space Path Loss
Loss (dB)=36.6+20LOG(FreqMhz)+20LOG(Dist Miles)
Great for calculating if there is nothing in the way (including air) but a worthwhile place to start.
20 miles at 2.4GHz = 130dB

## Slide 5: Propagation Anomalies
Normal Propagation
Anomalous Propagation

## Slide 6: Atmospheric Multipath
Multipath causes fading
If the combination of all incoming signals are in phase, enhancement occurs..if out of phase (e.g. near –180 degrees), attenuation occurs.
The shorter the wavelength, the more pronounced this may become

## Slide 7: Propagation Anomalies
Ducting
Subrefractive
Super refractive

## Slide 8: What causes the LOS multipath?
Temperature, moisture and pressure
Weather service soundings indicate the “current” state of what’s going on above
Temperature
Dewpoint
Pressure Height
Lines of equal Temp.
30º
40º
20º
10º
0º
-10º
-20º
-30º
The culprit

## Slide 9: Normal Propagation
K Factor = Curvature of the Earth
Fresnel Zone

## Slide 10
Fresnel Zone
Fresnel Zone Clearance
Reflection causing multipath
Ground Reflections / Refractions / Multi-Path

## Slide 11: Path Clearance

## Slide 12: Fresnel Zones
Caused by diffraction by objects in path
Even zones attenuate, odd enhance
Fresnel zone radius calculation
Conventional practice is to ensure about a 0.6 Fresnel zone clearance along path which provides best compromise to avoid deep nulls. Don’t put antenna up too high!
d1=distance to transmitter in miles
d2=distance to receiver in miles
FGHz=Frequency in Gigahertz

## Slide 13: Fresnel Clearance
Blue Vertical line indicates 0.6 Fresnel zone clearance at highest obstacle. Trees or buildings not modeled in this path, but must be included.
1.0, 1.5, and 1.75 Fresnel zones depicted on Radiomobile tool. No surface features are automatically assumed in Radiomobile, but they can be modeled. See the Yahoo Group entitled Radio_Mobile_Deluxe and check out file profile.zip
Antennas can be too high for reliable microwave paths

## Slide 14: Other considerations
On 3 mile paths or less, only FSL need be considered
Recommended that minimum 5dB margin be applied for miscellaneous other losses
Atmospheric and moisture attenuation becomes highly evident above 10 GHz
Heavy rain can cause some signal distortion as low as 2 GHz

## Slide 15: Rain Fade Risks By Region
Region 1 = Worst
Region 7 = Better

## Slide 16: Path availability
Barnett’s emprical fade estimate
Intended to estimate % of time in a year where fade exceeds a specified depth below free space for a given path and frequency
Pmf(%)=0.00006 x abfd3 x 10(-M/10)
Example: North Texas
A=1
B=0.333
F=2.43 GHz
D=40km
Fade margin= 20 dB
0.031% unavailability per year
Or 270 hours
From Freeman pp 64-65

## Slide 17: Link Budget
Link budgets are a tool to plan RF links. They are not guarantees of success.
Power (dBm) = 10 * LOG (PWR in mW)
Power (mW) = 10 (PWR in dBm/10)

## Slide 18: Radio Mobile
Freeware by Roger Coude, VE2DBE
Highly useful for tool RF coverage and path analysis
Allows quick analysis of Fresnel clearance
Uses elevation data from shuttle radar topography mission
http://www.cplus.org/rmw/english1.html

## Slide 19: Frequency Congestion
The number of channels available is finite
On 2.4 and 5.7 GHz, we must compete with part 15 devices. Even though we have “rights” to the frequencies, it will be difficult to clear them
As amateurs, we must consider using 802.11 on other bands (33cm, 23cm, 13cm, 6cm, 3cm, and up)
We must also remember to respect band plans and not interfere with weak signal operations.
There is plenty bandwidth for all…at least for now

## Slide 20: Unlicensed Spectrum
FCC Part 15
"……. operators of spread spectrum transmitters are reminded that the operation of Part 15 devices is subject to the conditions that any received interference, including interference from ISM operations, must be accepted and that harmful interference may not be caused to other radio services.
Should the operation of these systems cause harmful interference, the operator of the Part 15 system is required to correct the interference problem, even if such correction requires the cessation of operation of the Part 15 transmitter.
Thus, the Commission strongly recommends that utilities, cellular stations, public safety services, government agencies and others that employ Part 15 transmission systems to provide critical communication services should exercise due caution to determine if there are any nearby radio services that could be affected by their communications.”

## Slide 21: References
Freeman, Roger L. Radio System Design for Telecommunications (1-100 GHz), John Wiley and Sons, Inc. 1987