## Slide 1
Building the W7PUA DSP10 144MHz Transceiver
Dave Robinson, WW2R
Presented at Ham-com June 2004

## Slide 2: Original Design
Design by Bob Larkin W7PUA
Published in Sep-Nov 1999 QST
Covers 144 to 148MHz USB/LSB/FM/Others
Computer controlled through RS232 port
Can be locked to external 10MHz reference

## Slide 3: Features
Coverage from 144 to 148 MHz, USB, LSB, CW, and FM operation
1 Hz frequency control (except FM)
Full integration of UHF/Microwave transverters
I-F and audio is defined in software (SDR) to allow additions and improvements
Low-power 20+ milliwatt with an add-on 8-Watt amplifier
Eight audio filters including One audio filter custom tailored from the screen
LMS noise-reduction and auto-notch
Two selectable I-F bandwidths
Fully defineable spectral analysis, Spectral Waterfall display
Screen saves built in
Timed (Beacon) transmit and receive control
Precise EME (Moonbounce) Doppler correction of frequency for all modes
Real-time Moon and Sun tracking in Az, El and distance
Complete CW sending from the PC keyboard.
S-meter that is accurate from -140 to -25 dBm
Provision for frequency control to a fraction of a Hertz
Highly accurate Sun (and Moon) noise measurements

## Slide 4: Computer Requirements
Computer controls DSP-10, it doesn’t do much processing
This is different from the AC5OG FlexRadio where the computer does the number crunching….600MHz+ machine required
I successfully use a 75MHz ThinkPad
DOS currently required (Don’t use DOS window under another OS, others working this issue)

## Slide 5: Block Diagram

## Slide 6: My construction History
Mar 2001: Bought all components
Jan 5 2004: sent to work in NC for 2 weeks, decided could use all that spare evening time to stuff PCB rather than watching HBO!
Jan 21-24 2004: Return and finish construction
Jan 25: DSP-10 QRV
May 5: Added 30W Amplifier

## Slide 7: Finished DSP10

## Slide 8: EZ-LITE DSP board

## Slide 9: External 30W AMP
Uses Mitsubishi RA30H1317 Power module (30W output)

## Slide 10: DSP-10 with 30W Amp

## Slide 11: W5HN 144MHz

## Slide 12: W5HN 902MHz

## Slide 13: W5HN 1296MHz

## Slide 14: “OLD” NT5NT 10GHz

## Slide 15: “NEW” NT5NT 10G beacon

## Slide 16: 10368.000000MHz GPS REF

## Slide 17: Developments
Ez-Lite board discontinued, replacement is now $242 (was $99!)
Lyle Johnson KK7P developed replacement DSP board (“DSPX”, built) and interface board to DSP10 (“KDSP10”, kit) total $139
DSPX has lower power consumption and more powerful DSP.

## Slide 18: DSPX

## Slide 19: Next Steps
Engineer easier switching between internal/external 10MHz references
Use with external Microwave Modules transverter to enable 435MHz operation (5/10/24/47G IF) (need to lock 435/144 xverter Oscillator to GPS)
LCD/PIC tuning/mode selection

## Slide 20: Resources
W7PUA DSP-10 web site:-
http://www.proaxis.com/~boblark/dsp10.htm
KK7P DSPX:-
http://www.fidalgo.net/~wa7gxd/kdsp10.html
TAPR SITE:-
http://www.tapr.org/tapr/html/Fdsp10.html
Construction pictures:-
http://www.aa1yn.com/dsp-10/index.html
KA7EXM Alignment procedures/software:-
http://users.easystreet.com/rhayward/dsp10/pll_tuneup.html